## Slide 1: Configure Routers for Syslog, NTP, SSH
Network Security

## Slide 2: Configure Routers for Syslog, NTP, SSH
Objectives of the Topic
After completing this topic, a student will be able to
  Configure Cisco Routers for Syslog, NTP, and SSH in Packet tracer.

## Slide 3: Configure Routers for Syslog, NTP, SSH
Figures and material in this topic have been adapted from
Chapter 2: PT Activity: Configure Cisco Routers for Syslog, NTP, and SSH Operations – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure Routers for Syslog, NTP, SSH
Routers on a network can get their time settings synchronized with an NTP server via the Network Time Protocol (NTP).
Obtaining time and date information from a single source will allow a group of NTP clients to have more consistent time settings.
Routers can update their hardware clock using NTP, timestamp the log messages and send them to the Syslog server.

## Slide 5: Configure Routers for Syslog, NTP, SSH
Displaying the correct time and date in Syslog messages makes their analysis easier.
This helps in troubleshooting the network problems and attacks.
Secure Shell (SSH) is used to encrypt information over a network link and is used to authenticate a remote computer.

## Slide 6: Configure Routers for Syslog, NTP, SSH
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 7: Configure Routers for Syslog, NTP, SSH

## Slide 8: Configure Routers for Syslog, NTP, SSH
R2 is an ISP and is connected to two remote networks: R1 and R3.
Since R3 is a managed router, the ISP needs access to R3 for occasional troubleshooting or updates. This access is provided in a secure fashion by using Secure Shell (SSH).
In this activity, we will configure NTP and Syslog on all routers while SSH will be configured on R3.
The servers have been pre-configured for NTP and Syslog services.

## Slide 9: Configure Routers for Syslog, NTP, SSH
Furthermore, the routers are pre-configured with the following:
Enable password: ciscoenpa55
Password for vty lines: ciscovtypa55
Static routing

## Slide 10: Configure Routers for Syslog, NTP, SSH
Task 1: Configure routers as NTP Clients.
Step 1. Test Connectivity
Ping from PC-C to R3.

## Slide 11: Configure Routers for Syslog, NTP, SSH
Ping from R2 to R3. Telnet from PC-C to R3. Exit the Telnet session. Telnet from R2 to R3. Exit the Telnet session.

## Slide 12: Configure Routers for Syslog, NTP, SSH
Step 2. Configure R1, R2 and R3 as NTP clients.
R1(config)# ntp server 192.168.1.5
Use the command show ntp status to verify client configuration.
Repeat it for R2 and R3.

## Slide 13: Configure Routers for Syslog, NTP, SSH

## Slide 14: Configure Routers for Syslog, NTP, SSH
Step 3. Configure routers to update hardware clock.
R1(config)# ntp update-calendar
Use the command show clock to verify that the hardware clock was updated.
Do the same for R2 and R3.

## Slide 15: Configure Routers for Syslog, NTP, SSH

## Slide 16: Configure Routers for Syslog, NTP, SSH
Step 4. Configure routers to timestamp log messages.
R1(config)# service timestamps log datetime msec
Do the same for R2 and R3

## Slide 17: Configure Routers for Syslog, NTP, SSH
Task 2: Configure routers to log messages to the Syslog Server.
Step 1. Configure the routers to identify the Syslog server. Do same for R2, R3.
R1(config)# logging host 192.168.1.6
Step 2. Verify logging configuration using the command show logging.
Step 3. Examine logs of the Syslog server.
From the Config tab of the Syslog server’s dialogue box, select Syslog services button.

## Slide 18: Configure Routers for Syslog, NTP, SSH

## Slide 19: Configure Routers for Syslog, NTP, SSH
Task 3: Configure R3 to support SSH connections.
Step 1. Configure a domain name of ccnasecurity.com on R3.
R3(config)# ip domain-name ccnasecurity.com
Step 2. Configure users for login from the SSH client on R3. user ID = SSHadmin, Password = ciscosshpa55. Highest possible privilege level .
R3(config)# username SSHadmin privilege 15 secret ciscosshpa55

## Slide 20: Configure Routers for Syslog, NTP, SSH
Step 3. Configure the incoming VTY lines on R3.
Use the local user accounts for mandatory login and validation. Accept only SSH connections.
R3(config)# line vty 0 4
R3(config-line)# login local
R3(config-line)# transport input ssh

## Slide 21: Configure Routers for Syslog, NTP, SSH
Step 4. Erase existing key pairs on R3.
R3(config)#crypto key zeroize rsa
% No Signature RSA Keys found in configuration.
Step 5. Generate the RSA encryption key pair for R3.
The router uses the RSA key pair for authentication and encryption of transmitted SSH data. Configure the RSA keys with a modulus of 1024. The default is 512, and the range is from 360 to 2048.

## Slide 22: Configure Routers for Syslog, NTP, SSH

## Slide 23: Configure Routers for Syslog, NTP, SSH
Step 6. Verify the SSH configuration.
Use the show ip ssh command to see the current settings.
Verify that the default values of authentication timeout and retries are 120 and 3.

## Slide 24: Configure Routers for Syslog, NTP, SSH
Step 7. Configure SSH timeouts and authentication parameters.
Set the timeout to 90 seconds, the number of authentication retries to 2, and the version to 2.
R3(config)# ip ssh time-out 90
R3(config)# ip ssh authentication-retries 2
R3(config)# ip ssh version 2
To confirm that the values have been updated, issue the show ip ssh command.

## Slide 25: Configure Routers for Syslog, NTP, SSH
Step 8. Attempt to connect to R3 via Telnet from PC-C.
From the Command Prompt icon of PC-C, enter
PC> telnet 192.168.3.1
As R3 has been configured to accept only SSH connections, this connection should fail.
Step 9. Connect to R3 using SSH on PC-C.
PC> ssh –l SSHadmin 192.168.3.1
When prompted for the password, enter ciscosshpa55.

## Slide 26: Configure Routers for Syslog, NTP, SSH
Step 10. Connect to R3 using SSH on R2.
In order to troubleshoot and maintain the R3 router, the administrator at the ISP must use SSH to access the router CLI.
R2# ssh –v 2 –l SSHadmin 10.2.2.1
When prompted for the password, enter the password configured for the administrator: ciscosshpa55.

## Slide 27: Configure Routers for Syslog, NTP, SSH
Step 11. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End