## Slide 1: Configure AAA Authentication on Routers
Network Security

## Slide 2: Configure AAA Authentication on Routers
Objectives of the Topic
After completing this topic, a student will be able to
  Configure AAA Authentication on Cisco Routers in Packet tracer.

## Slide 3: Configure AAA Authentication on Routers
Figures and material in this topic have been adapted from
Chapter 3: PT Activity: Configure AAA Authentication on Cisco Routers – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure AAA Authentication on Routers
“Authentication asks the question, "Who or what are you?" Authorization asks, "What are you allowed to do?" And finally, accounting wants to know, "What did you do?“”
Remote Authentication Dial-In User Service (RADIUS) and Terminal Access Controller Access Control System (TACACS)– most widely accepted AAA protocol. RADIUS is an Internet standard.
Sean Convery, “Network Authentication, Authorization, and Accounting: Part One” - The Internet Protocol Journal Volume 10, No. 1, 2007

## Slide 5: Configure AAA Authentication on Routers
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 6: Configure AAA Authentication on Routers

## Slide 7: Configure AAA Authentication on Routers
The task is to configure and test local and server-based AAA solutions.
We will create a local user account and configure local AAA on router R1 to test the console and VTY logins.
User account: Admin1 and password admin1pa55
Then, we will configure router R2 to support server-based authentication using the TACACS+ protocol.

## Slide 8: Configure AAA Authentication on Routers
The TACACS+ server has been pre-configured with the following:
Client: R2 using the keyword tacacspa55
User account: Admin2 and password admin2pa55
Finally, we will configure router R3 to support server-based authentication using the RADIUS protocol.
The RADIUS server has been pre-configured with the following:

## Slide 9: Configure AAA Authentication on Routers
Client: R3 using the keyword radiuspa55
User account: Admin3 and password admin3pa55
The routers have also been pre-configured with the following:
Enable secret password: ciscoenpa55
RIP version 2

## Slide 10: Configure AAA Authentication on Routers
Task 1: Configure Local AAA Authentication for Console Access on R1
Step 1. Test connectivity.
Ping from PC-A to PC-B. Ping from PC-A to PC-C. Ping from PC-B to PC-C.
Step 2. Configure a local username on R1.
R1(config)# username Admin1 password admin1pa55
Step 3. Configure local AAA authentication for console access on R1.

## Slide 11: Configure AAA Authentication on Routers
Enable AAA on R1 and configure AAA authentication for console login to use the local database.
R1(config)# aaa new-model
R1(config)# aaa authentication login default local
Step 4. Configure the line console to use the defined AAA authentication method.
R1(config)# line console 0
R1(config-line)# login authentication default

## Slide 12: Configure AAA Authentication on Routers

## Slide 13: Configure AAA Authentication on Routers
Step 5. Verify the AAA authentication method.

## Slide 14: Configure AAA Authentication on Routers
Task 2: Configure Local AAA Authentication for VTY Lines on R1
Step 1. Configure a named list AAA authentication method for VTY lines on R1.
Configure a named list called TELNET-LOGIN to authenticate logins using local AAA.
R1(config)# aaa authentication login TELNET-LOGIN local

## Slide 15: Configure AAA Authentication on Routers
Step 2. Configure the VTY lines to use the defined AAA authentication method.
R1(config)# line vty 0 4
R1(config-line)# login authentication TELNET-LOGIN
R1(config-line)# end
Step 3. Verify the AAA authentication method.
Verify the Telnet configuration.
From command prompt of PC-A, Telnet to R1. PC> telnet 192.168.1.1

## Slide 16: Configure AAA Authentication on Routers

## Slide 17: Configure AAA Authentication on Routers
Task 3: Configure Server-Based AAA Authentication Using TACACS+ on R2
Step 1. Configure a backup local database entry called Admin.
For backup purposes, configure a local username of Admin and secret password of adminpa55.
R2(config)# username Admin password adminpa55

## Slide 18: Configure AAA Authentication on Routers
Step 2. Verify the TACACS+ Server configuration.
Select the TACACS+ Server. From the Config tab, click on AAA and notice that there is a Network configuration entry for R2 and a User Setup entry for Admin2.
Step 3. Configure the TACACS+ server specifics on R2.
R2(config)# tacacs-server host 192.168.2.2
R2(config)# tacacs-server key tacacspa55

## Slide 19: Configure AAA Authentication on Routers
Step 4. Configure AAA login authentication for console access on R2.
Enable AAA on R2 and configure all logins to authenticate using the AAA TACACS+ server and if not available, then use the local database.
R2(config)# aaa new-model
R2(config)# aaa authentication login default group tacacs+ local

## Slide 20: Configure AAA Authentication on Routers
Step 5. Configure the line console to use the defined AAA authentication method.
R2(config)# line console 0
R2(config-line)# login authentication default

## Slide 21: Configure AAA Authentication on Routers
Step 6. Verify the AAA authentication method.
Verify the user EXEC login using the AAA TACACS+ server.

## Slide 22: Configure AAA Authentication on Routers
Task 4: Configure Server-Based AAA Authentication Using RADIUS on R3
Step 1. Configure a backup local database entry called Admin.
R3(config)# username Admin password adminpa55
Step 2. Verify RADIUS configuration.
Select the RADIUS Server.

## Slide 23: Configure AAA Authentication on Routers
From the Config tab, click on AAA and notice that there is a Network configuration entry for R3 and a User Setup entry for Admin3.
Step 3. Configure the RADIUS server specifics on R3.
Configure the AAA RADIUS server IP address and secret key on R3.
R3(config)# radius-server host 192.168.3.2
R3(config)# radius-server key radiuspa55

## Slide 24: Configure AAA Authentication on Routers
Step 4. Configure AAA login authentication for console access on R3.
R3(config)# aaa new-model
R3(config)# aaa authentication login default group radius local
Step 5. Configure the line console to use defined AAA authentication method.
R3(config)# line console 0
R3(config-line)# login authentication default

## Slide 25: Configure AAA Authentication on Routers
Step 6. Verify the AAA authentication method.
Verify the user EXEC login using the AAA TACACS+ server.

## Slide 26: Configure AAA Authentication on Routers
Step 7. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End