## Slide 1: Configure IP ACLs to Mitigate Attacks
Network Security

## Slide 2: Configure IP ACLs to Mitigate Attacks
Objectives of the Topic
After completing this topic, a student will be able to
  Configure IP ACLs to Mitigate Attacks in Packet tracer.

## Slide 3: Configure IP ACLs to Mitigate Attacks
Figures and material in this topic have been adapted from
Chapter 4: PT Activity: Configure IP ACLs to Mitigate Attacks – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure IP ACLs to Mitigate Attacks
“Cisco provides basic traffic filtering capabilities with access control lists (ACL). Access lists filter network traffic by controlling whether routed packets are forwarded or blocked at the router’s interfaces. Your router examines each packet to determine whether to forward or drop the packet, on the basis of the criteria you specified within the access lists: source address, destination address of the traffic, the upper-layer protocol, or other information”.
“Cisco IOS Security Configuration Guide” – Cisco Systems, Inc, 2006

## Slide 5: Configure IP ACLs to Mitigate Attacks
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 6: Configure IP ACLs to Mitigate Attacks

## Slide 7: Configure IP ACLs to Mitigate Attacks
Access to routers R1, R2, and R3 should only be permitted from PC-C, the management station.
PC-C is also used for connectivity testing to PC-A, a server providing DNS, SMTP, FTP, and HTTPS services.
The standard procedure is to apply ACLs on edge routers to mitigate common threats based on source and/or destination IP address.
We will create ACLs on edge routers R1 and R3 to achieve this goal and then verify ACL functionality from internal and external hosts.

## Slide 8: Configure IP ACLs to Mitigate Attacks
The routers have been pre-configured with:
Enable password: ciscoenpa55
Password for console: ciscoconpa55
Username for VTY lines: SSHadmin
Password for VTY lines: ciscosshpa55
IP addressing
Static routing

## Slide 9: Configure IP ACLs to Mitigate Attacks
Task 1: Verify Basic Network Connectivity
Step 1. From the PC-C command prompt, ping the PC-A server.
Step 2. From the PC-C command prompt, SSH to the router R2 Lo0 interface. Exit the SSH session.

## Slide 10: Configure IP ACLs to Mitigate Attacks
PC> ssh –l SSHadmin 192.168.2.1
Password: ciscosshpa55

## Slide 11: Configure IP ACLs to Mitigate Attacks
Step 3. From PC-C, open a web browser to the PC-A server (using the IP address) to display the web page. Close the browser on PC-C .
Step 4. From the PC-A server command prompt, ping PC-C .

## Slide 12: Configure IP ACLs to Mitigate Attacks

## Slide 13: Configure IP ACLs to Mitigate Attacks
Task 2: Secure Access to Routers
Step 1. Configure ACL 10 to block all remote access to the routers except from PC-C.
Use the access-list command to create a numbered IP ACL on R1, R2, and R3.
R1(config)# access-list 10 permit 192.168.3.3 0.0.0.0
Do the same for R2 and R3.
Step 2. Apply ACL 10 to ingress traffic on the VTY lines .

## Slide 14: Configure IP ACLs to Mitigate Attacks
Use the access-class command to apply the access list to incoming traffic on the VTY lines.
R1(config-line)# access-class 10 in
Repeat for R2 and R3.
Step 3. Verify exclusive access from management station PC -C.
SSH to 192.168.2.1 from PC-C (should be successful). SSH to 192.168.2.1 from PC-A (should fail).
PC> ssh –l SSHadmin 192.168.2.1

## Slide 15: Configure IP ACLs to Mitigate Attacks
Task 3: Create a Numbered IP ACL 100 :
On R3, block all packets containing the source IP address from pool of addresses: 127.0.0.0/8, any RFC 1918 private addresses, and any IP multicast address.
Step 1. Configure ACL 100 to block all specified traffic from the outside network.
You should also block traffic sourced from your own internal address space if it is not an RFC 1918 address.

## Slide 16: Configure IP ACLs to Mitigate Attacks
R3(config)# access-list 100 deny ip 10.0.0.0 0.255.255.255 any
R3(config)# access-list 100 deny ip 172.16.0.0 0.15.255.255 any
R3(config)# access-list 100 deny ip 192.168.0.0 0.0.255.255 any
R3(config)# access-list 100 deny ip 127.0.0.0 0.255.255.255 any
R3(config)# access-list 100 deny ip 224.0.0.0 15.255.255.255 any
R3(config)# access-list 100 permit ip any any

## Slide 17: Configure IP ACLs to Mitigate Attacks
Step 2. Apply the ACL to interface Serial 0/0/1.
Use ip access-group command to apply access list to incoming traffic on interface Serial 0/0/1.
R3(config)# interface s0/0/1
R3(config-if)# ip access-group 100 in
Step 3. Confirm that the specified traffic entering interface Serial 0/0/1 is dropped.
From the PC-C command prompt, ping the PC-A server. The ICMP echo replies are blocked by the ACL.

## Slide 18: Configure IP ACLs to Mitigate Attacks
Step 4. Remove the ACL from interface Serial 0/0/1.
Remove ACL to allow traffic from the outside network.
Use the no ip access-group command to remove the access list from interface Serial 0/0/1.
R3(config)# interface s0/0/1
R3(config-if)# no ip access-group 100 in

## Slide 19: Configure IP ACLs to Mitigate Attacks
Task 4: Create a Numbered IP ACL 110
Deny all outbound packets with source address outside the range of internal IP addresses.
Step 1. Configure ACL 110 to permit only traffic from the inside network.
R3(config)# access-list 110 permit ip 192.168.3.0 0.0.0.255 any
Step 2. Apply the ACL to interface F0/1.
R3(config)# interface fa0/1
R3(config-if)# ip access-group 110 in

## Slide 20: Configure IP ACLs to Mitigate Attacks
Task 5: Create a Numbered IP ACL 120:
Permit any outside host to access DNS, SMTP, and FTP services on server PC-A, deny any outside host access to HTTPS services on PC-A, and permit PC-C to access R1 via SSH.
Step 1. Verify that PC-C can access the PC-A via HTTPS using the web browser.
Disable HTTP and enable HTTPS on server PC-A.
Step 2. Configure ACL 120 to specifically permit and deny the specified traffic.

## Slide 21: Configure IP ACLs to Mitigate Attacks
R1(config)# access-list 120 permit udp any host 192.168.1.3 eq domain
R1(config)# access-list 120 permit tcp any host 192.168.1.3 eq smtp
R1(config)# access-list 120 permit tcp any host 192.168.1.3 eq ftp
R1(config)# access-list 120 deny tcp any host 192.168.1.3 eq 443
R1(config)# access-list 120 permit tcp host 192.168.3.3 host 10.1.1.1 eq 22

## Slide 22: Configure IP ACLs to Mitigate Attacks
Step 3. Apply the ACL to interface S0/0/0.
R1(config)# interface s0/0/0
R1(config-if)# ip access-group 120 in
Step 4. Verify that PC-C cannot access PC-A via HTTP using the web browser.
Task 6: Modify An Existing ACL:
Permit ICMP echo replies and destination unreachable messages from the outside network (relative to R1); deny all other incoming ICMP packets.

## Slide 23: Configure IP ACLs to Mitigate Attacks
Step 1. Verify that PC-A cannot success fully ping the loopback interface on R2.
Step 2. Make any necessary changes to ACL 120 to permit and deny the specified traffic.
R1(config)# access-list 120 permit icmp any any echo-reply
R1(config)# access-list 120 permit icmp any any unreachable
R1(config)# access-list 120 deny icmp any any
R1(config)# access-list 120 permit ip any any

## Slide 24: Configure IP ACLs to Mitigate Attacks
Step 3. Verify that PC-A can successfully ping the loopback interface on R2.
Step 4. Check results .
Your completion percentage should be 100%.
Click Check Results to see feedback.
End