## Slide 1: Configure Context-Based Access Control
Network Security

## Slide 2: Configure Context-Based Access Control
Objectives of the Topic
After completing this topic, a student will be able to
  Configure Context-Based Access Control in Packet tracer.

## Slide 3: Configure Context-Based Access Control
Figures and material in this topic have been adapted from
Chapter 4: PT Activity: Configuring Context-Based Access Control (CBAC) – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure Context-Based Access Control
“Context-Based Access Control (CBAC) provides advanced traffic filtering functionality and can be used as an integral part of your network’s firewall. CBAC works to provide network protection on multiple levels using the following functions: Traffic Filtering, Traffic Inspection, Alerts and Audit Trails, and Intrusion Detection”
“Cisco IOS Security Configuration Guide” – Cisco Systems, Inc, 2006

## Slide 5: Configure Context-Based Access Control
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 6: Configure Context-Based Access Control

## Slide 7: Configure Context-Based Access Control
Context-Based Access Control (CBAC) is used to create an IOS firewall.
In this activity, we will create a basic CBAC configuration on edge router R3 that provides access to resources outside of the network for hosts on the inside network.
R3 blocks external hosts from accessing internal resources.

## Slide 8: Configure Context-Based Access Control
The routers have been pre-configured:
Enable password: ciscoenpa55
Password for console: ciscoconpa55
Password for vty lines: ciscovtypa55
IP addressing
Static routing
All switch ports are in VLAN 1 for switches S1 and S3.

## Slide 9: Configure Context-Based Access Control
Task 1: Block Traffic From Outside
Step 1. Verify Basic Network Connectivity.
From the PC-C command prompt, ping the PC-A server. From the PC-C command prompt, Telnet to the Router R2 S0/0/1 interface: IP address 10.2.2.2. Exit the Telnet session.
From PC-C, open a web browser to the PC-A server to display the web page. Close the browser on PC-C.
From PC-A server command prompt, ping PC-C.

## Slide 10: Configure Context-Based Access Control
Step 2. Configure a named IP ACL on R3 to block all traffic originating from the outside network.
Use the ip access-list extended command to create a named IP ACL.
R3(config)# ip access-list extended OUT-IN
R3(config-ext-nacl)# deny ip any any
R3(config-ext-nacl)# exit
Step 3. Apply the ACL to interface Serial 0/0/1.
R3(config)# interface s0/0/1

## Slide 11: Configure Context-Based Access Control
R3(config-if)# ip access-group OUT-IN in
Step 4. Confirm that traffic entering interface Serial 0/0/1 is dropped.
From the PC-C command prompt, ping the PC-A server.
The ICMP echo replies are blocked by the ACL.
Task 2: Create a CBAC Inspection Rule
Step 1. Create an inspection rule to inspect ICMP, Telnet, and HTTP traffic.

## Slide 12: Configure Context-Based Access Control
R3(config)# ip inspect name IN-OUT-IN icmp
R3(config)# ip inspect name IN-OUT-IN telnet
R3(config)# ip inspect name IN-OUT-IN http
Step 2. Turn on time-stamped logging and CBAC audit trail messages.
Use the ip inspect audit-trail command to turn on CBAC audit messages to provide a record of network access through the firewall, including illegitimate access attempts.

## Slide 13: Configure Context-Based Access Control
Enable logging to the syslog server, 192.168.1.3, with the logging host command. Make sure that logged messages are time stamped.
R3(config)# ip inspect audit-trail
R3(config)# service timestamps debug datetime msec
R3(config)# logging host 192.168.1.3
Step 3. Apply the inspection rule to egress traffic on interface S 0/0/1.
R3(config-if)# ip inspect IN-OUT-IN out

## Slide 14: Configure Context-Based Access Control
Step 4. Verify that audit trail messages are being logged on the syslog server.
From PC-C, test connectivity to PC-A with ping, Telnet, and HTTP. Ping and HTTP should be successful. PC-A will reject the Telnet session.
From PC-A, test connectivity to PC-C with ping and Telnet. All should be blocked.

## Slide 15: Configure Context-Based Access Control
Review the syslog messages on server PC-A: click the Config tab and then click the SYSLOG.

## Slide 16: Configure Context-Based Access Control
Task 3: Verify Firewall Functionality
Step 1. Open a Telnet session from PC-C to R2.
The Telnet should succeed. While the Telnet session is active, issue the command show ip inspect sessions on R3. This command displays the existing sessions that are currently being tracked and inspected by CBAC.
R3# show ip inspect sessions
Session 145976424 (192.168.3.3:1029)=> (10.1.1.2:23) telnet SIS_OPEN

## Slide 17: Configure Context-Based Access Control
What is the source IP address and port number? 192.168.3.3:1029 (port 1029 is random)
What is the destination IP address and port number? 10.1.1.2:23 (Telnet = port 23)
Exit the Telnet session
Step 2. From PC-C, open a web browser to the PC-A server web page using the server IP address.

## Slide 18: Configure Context-Based Access Control
The HTTP session should succeed. While the HTTP session is active, issue the command show ip inspect sessions on R3.
R3# show ip inspect sessions
Established Sessions: Session 104637440
(192.168.3.3:1033)=>(192.168.1.3:80) http SIS_OPEN
Source IP/port number=> destination IP/port number.
Close the browser on PC-C.

## Slide 19: Configure Context-Based Access Control
Step 3. View the interface configuration and inspection rule timers.
Enter the show ip inspect interfaces command on R3. The output shows existing sessions that are currently being tracked and inspected by CBAC.

## Slide 20: Configure Context-Based Access Control
Task 4: Review CBAC Configuration
Step 1. Display CBAC configuration.
Enter the show ip inspect config command on R3 to display the complete CBAC inspection configuration.

## Slide 21: Configure Context-Based Access Control

## Slide 22: Configure Context-Based Access Control
Step 2. Display real-time output that can be used for troubleshooting.
Enter the debug ip inspect detailed command on R3 to display detailed messages about CBAC software events, including information about CBAC packet processing.
From PC-C, open a web browser; enter the PC-A (server) IP address: 192.168.1.3.

## Slide 23: Configure Context-Based Access Control

## Slide 24: Configure Context-Based Access Control
Step 3. Check Results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End