## Slide 1: Configure a Zone-Based Policy Firewall
Network Security

## Slide 2: Configure a Zone-Based Policy Firewall
Objectives of the Topic
After completing this topic, a student will be able to
  Configure a Zone-Based Policy Firewall in Packet tracer.

## Slide 3: Configure a Zone-Based Policy Firewall
Figures and material in this topic have been adapted from
Chapter 4: PT Activity: Configuring a Zone-Based Policy Firewall (ZPF) – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure a Zone-Based Policy Firewall
“Zone-based policy (ZPF) firewalls are the latest development in the evolution of Cisco firewall technologies. Interfaces are assigned to zones, and inspection policy is applied to traffic moving between the zones. Inter-zone policies offer considerable flexibility and granularity, so different inspection policies can be applied to multiple host groups connected to the same router interface.”
“Zone−Based Policy Firewall Design and Application Guide” – Document ID: 98628, Cisco Systems, Inc, 2010

## Slide 5: Configure a Zone-Based Policy Firewall
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 6: Configure a Zone-Based Policy Firewall

## Slide 7: Configure a Zone-Based Policy Firewall
In this activity, we will configure a basic ZPF on an edge router R3 that allows internal hosts access to external resources and blocks external hosts from accessing internal resources.
The routers have been pre-configured:
Console password: ciscoconpa55
Password for vty lines: ciscovtypa55
Enable password: ciscoenpa55
Host names,
IP addressing, and Static routing

## Slide 8: Configure a Zone-Based Policy Firewall
Task 1: Verify Basic Network Connectivity
Step 1. From the PC-A command prompt, ping PC-C at 192.168.3.3.
Step 2. From the PC-C command prompt, Telnet to the Router R2 S0/0/1 interface at 10.2.2.2. Exit the Telnet session.
Step 3. From PC-C, open a web browser to the PC-A server. Click the Desktop tab and click the Web Browser application. Enter the PC-A IP address 192.168.1.3 as the URL. Close the browser on PC-C.

## Slide 9: Configure a Zone-Based Policy Firewall
Task 2: Create the Firewall Zones on R3
Step 1. Create an internal zone.
Use the zone security command to create a zone named IN-ZONE.
R3(config)# zone security IN-ZONE
Step 2. Create an external zone.
R3(config-sec-zone)# zone security OUT-ZONE
R3(config-sec-zone)# exit

## Slide 10: Configure a Zone-Based Policy Firewall
Task 3: Define a Traffic Class and Access List
Step 1. Create an ACL that defines internal traffic.
Use the access-list command to create extended ACL 101 to permit all IP protocols from the 192.168.3.0/24 source network to any destination.
R3(config)# access-list 101 permit ip 192.168.3.0 0.0.0.255 any

## Slide 11: Configure a Zone-Based Policy Firewall
Step 2. Create a class map referencing the internal traffic ACL.
Use the class map type inspect command with the match-all option to create a class map named IN-NETCLASS-MAP. Use the match access-group command to match ACL 101.
R3(config)# class-map type inspect match-all IN-NET-CLASS-MAP
R3(config-cmap)# match access-group 101
R3(config-cmap)# exit

## Slide 12: Configure a Zone-Based Policy Firewall
Task 4: Specify Firewall Policies
Step 1. Create a policy map to determine what to do with matched traffic.
Use the policy-map type inspect command and create a policy map named IN-2-OUT-PMAP.
R3(config)# policy-map type inspect IN-2-OUT-PMAP
Step 2. Specify a class type of inspect and reference class map IN-NET-CLASS -MAP.

## Slide 13: Configure a Zone-Based Policy Firewall
R3(config-pmap)# class type inspect IN-NET-CLASS-MAP
Step 3. Specify the action of inspect for this policy map
The use of the inspect command invokes context-based access control.
R3(config-pmap-c)# inspect
%No specific protocol configured in class IN-NET-CLASS-MAP for inspection. All protocols will be inspected.

## Slide 14: Configure a Zone-Based Policy Firewall
Issue the exit command twice to leave config-pmap-c mode and return to config mode.
R3(config-pmap-c)# exit
R3(config-pmap)# exit

## Slide 15: Configure a Zone-Based Policy Firewall
Task 5: Apply Firewall Policies
Step 1. Create a pair of zones.
Using the zone-pair security command, create a zone pair named IN-2-OUT-ZPAIR. Specify the source and destination zones that were created in Task 1.
R3(config)# zone-pair security IN-2-OUT-ZPAIR source IN-ZONE destination OUT-ZONE
Step 2. Specify the policy map for handling the traffic between the two zones.

## Slide 16: Configure a Zone-Based Policy Firewall
Attach a policy-map and its associated actions to the zone pair using the service-policy type inspect command and reference the policy map previously created, IN-2-OUT-PMAP.
R3(config-sec-zone-pair)# service-policy type inspect IN-2-OUT-PMAP
R3(config-sec-zone-pair)# exit
Step 3. Assign interfaces to the appropriate security zones.

## Slide 17: Configure a Zone-Based Policy Firewall
Use the zone-member security command in interface config mode to assign Fa0/1 to IN-ZONE and S0/0/1 to OUT-ZONE.
R3(config)# interface fa0/1
R3(config-if)# zone-member security IN-ZONE
R3(config-if)# exit
R3(config)# interface s0/0/1
R3(config-if)# zone-member security OUT-ZONE
Step 4. Copy the running config to the startup config.

## Slide 18: Configure a Zone-Based Policy Firewall
Task 6: Test Firewall Functionality from IN-ZONE to OUT-ZONE
Verify that internal hosts can still access external resources after configuring the zone-based policy firewall.
Step 1. From internal PC-C, ping the external PC-A server.
From the PC-C Command Prompt, ping PC-A at 192.168.1.3. The ping should succeed.

## Slide 19: Configure a Zone-Based Policy Firewall
Step 2. From internal PC-C, Telnet to the router R2 S0/0/1 interface.
From the PC-C Command Prompt, telnet to R2 at 10.2.2.2 and provide the vty password ciscovtypa55.
The telnet should succeed. While the Telnet session is active, issue the command show policy-map type inspect zone-pair sessions on R3 to view established sessions.

## Slide 20: Configure a Zone-Based Policy Firewall
source IP/port number = 192.168.3.3:1025
destination IP/port number = 10.2.2.2:23

## Slide 21: Configure a Zone-Based Policy Firewall
Step 3. From PC-C, exit the Telnet session on R2 and close the Command Prompt window.
Step 4. From internal PC-C, open a web browser to the PC-A server web page.
Enter the server IP address 192.168.1.3 in the browser URL field and click Go.
The HTTP session should succeed. While the HTTP session is active, issue the command show policy-map type inspect zone-pair sessions on R3 to view established sessions.

## Slide 22: Configure a Zone-Based Policy Firewall
source IP/port number = 192.168.3.3:1027
destination IP/port number = 192.168.1.3:80

## Slide 23: Configure a Zone-Based Policy Firewall
Task 7: Test Firewall Functionality from OUT-ZONE to IN-ZONE
Verify that external hosts CANNOT access internal resources after configuring the zone-based policy firewall.
Step 1. From the PC-A server command prompt, ping PC-C at 192.168.3.3. The ping should fail.
Step 2. From router R2, ping PC-C at 192.168.3.3. The ping should fail.

## Slide 24: Configure a Zone-Based Policy Firewall
Step 3. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End