## Slide 1: Configure IOS Intrusion Prevention System
Network Security

## Slide 2: Configure IOS Intrusion Prevention System
Objectives of the Topic
After completing this topic, a student will be able to
  Configure IOS Intrusion Prevention System using CLI in Packet tracer.

## Slide 3: Configure IOS Intrusion Prevention System
Figures and material in this topic have been adapted from
Chapter 5: PT Activity: Configure IOS Intrusion Prevention System (IPS) using CLI – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure IOS Intrusion Prevention System
“Cisco IOS Intrusion Prevention System (IOS IPS) is used to manage intrusion prevention on Cisco routers. It acts as an in-line intrusion prevention sensor, watching packets and sessions as they flow through the router and scanning each packet to match any of the Cisco IOS IPS signatures. When it detects suspicious activity, it responds before network security can be compromised and logs the event through Cisco IOS syslog messages.”
“User Guide for Cisco Security Manager 4.1” – Cisco Systems, Inc, 2011

## Slide 5: Configure IOS Intrusion Prevention System
Experimental Setup: Lets assume a network topology consists of three routers R1, R2, and R3.

## Slide 6: Configure IOS Intrusion Prevention System

## Slide 7: Configure IOS Intrusion Prevention System
We want to configure router R1 for IPS in order to scan traffic entering the 192.168.1.0 network.
The server labeled ‘Syslog Server’ is used to log IPS messages. You must configure the router to identify the syslog server in order to receive logging messages. Displaying the correct time and date in syslog messages is vital when using syslog to monitor the network.
Set the clock and configure timestamp service for logging on the routers.

## Slide 8: Configure IOS Intrusion Prevention System
Finally, enable IPS to produce an alert and drop ICMP echo reply packets inline.
The server and PCs have been preconfigured.
The routers have also been preconfigured with the following:
Enable password: ciscoenpa55
Console password: ciscoconpa55
VTY line password: ciscovtypa55
Enhanced Interior Gateway Routing Protocol (EIGRP 101)

## Slide 9: Configure IOS Intrusion Prevention System
Task 1: Enable IOS IPS
Within Packet Tracer, the routers already have the signature files imported and in place. For this reason, it is not necessary to configure the public crypto key and complete a manual import of the signature files.
Step 1. Verify network connectivity.
Ping from PC-C to PC-A. The ping should be successful. Ping from PC-A to PC-C. The ping should be successful.

## Slide 10: Configure IOS Intrusion Prevention System
Step 2. Create an IOS IPS configuration directory in flash.
R1#mkdir ipsdir
Create directory filename [ipsdir]? <Enter>
Created dir flash:ipsdir
Step 3. Configure the IPS signature storage location.
On R1, configure the IPS signature storage location to be the directory you just created.
R1(config)#ip ips config location flash:ipsdir

## Slide 11: Configure IOS Intrusion Prevention System
Step 4. Create an IPS rule.
On R1, create an IPS rule name using the ip ips name name command in global configuration mode. Name the IPS rule iosips.
R1(config)# ip ips name iosips
Step 5. Enable logging.
IOS IPS supports the use of syslog to send event notification. Syslog notification is enabled by default. If logging console is enabled, you see IPS syslog messages.

## Slide 12: Configure IOS Intrusion Prevention System
Enable syslog if it is not enabled.
R1(config)# ip ips notify log
Use the clock set command from privileged EXEC mode to reset the clock if necessary.
R1# clock set 01:20:00 6 january 2009
Verify that the timestamp service for logging is enabled on the router using the show run command.
Enable the timestamp service if it is not enabled.

## Slide 13: Configure IOS Intrusion Prevention System
R1(config)# service timestamps log datetime msec
Send log messages to the Syslog server at IP address 192.168.1.50.
R1(config)# logging host 192.168.1.50
Step 6. Configure IOS IPS to use the signature categories.
Retire the all signature category with the retired true command (all signatures within the signature release).

## Slide 14: Configure IOS Intrusion Prevention System
Unretire the IOS_IPS Basic category with the retired false command.
R1(config)# ip ips signature-category
R1(config-ips-category)# category all
R1(config-ips-category-action)# retired true
R1(config-ips-category-action)# exit
R1(config-ips-category)# category ios_ips basic
R1(config-ips-category-action)# retired false
R1(config-ips-category-action)# exit
R1(config-ips-cateogry)# exit

## Slide 15: Configure IOS Intrusion Prevention System
Do you want to accept these changes? <Enter>
Step 7. Apply the IPS rule to an interface.
Apply the IPS rule to an interface with the ip ips name direction command in interface configuration mode. Apply the rule outbound on the Fa0/0 interface of R1. After you enable IPS, some log messages will be sent to the console line indicating that the IPS engines are being initialized.

## Slide 16: Configure IOS Intrusion Prevention System
The direction in means that IPS inspects only traffic going into the interface. Similarly, out means only traffic going out the interface.
R1(config)# interface fa0/0
R1(config-if)# ip ips iosips out

## Slide 17: Configure IOS Intrusion Prevention System
Task 2: Modify the Signature
Step 1. Change the event-action of a signature.
Un-retire the echo request signature (signature 2004, subsig ID 0), enable it and change the signature action to alert, and drop.
R1(config)# ip ips signature-definition
R1(config-sigdef)# signature 2004 0
R1(config-sigdef-sig)# status
R1(config-sigdef-sig-status)# retired false
R1(config-sigdef-sig-status)# enabled true

## Slide 18: Configure IOS Intrusion Prevention System
R1(config-sigdef-sig-status)# exit
R1(config-sigdef-sig)# engine
R1(config-sigdef-sig-engine)# event-action produce-alert
R1(config-sigdef-sig-engine)# event-action deny-packet-inline
R1(config-sigdef-sig-engine)# exit
R1(config-sigdef-sig)# exit
R1(config-sigdef)# exit
Do you want to accept these changes? <Enter>

## Slide 19: Configure IOS Intrusion Prevention System
Step 2. Use show commands to verify IPS .
Use the show ip ips all command to see an IPS configuration status summary. To which interfaces and in which direction is the iosips rule applied?
Fa0/0 outbound.

## Slide 20: Configure IOS Intrusion Prevention System
Fa0/0 outbound.

## Slide 21: Configure IOS Intrusion Prevention System
Step 3. Verify that IPS is working properly.
From PC-C, attempt to ping PC-A. Were the pings successful? Why or why not?
The pings should fail. This is because the IPS rule for event-action of an echo request was set to “deny-packet-inline”.

## Slide 22: Configure IOS Intrusion Prevention System
From PC-A, attempt to ping PC-C. Were the pings successful? Why or why not?
The ping should be successful. This is because the IPS rule does not cover echo reply. When PC-A pings PC-C, PC-C responds with an echo reply.
Step 4. View the Syslog messages.
Click on the Syslog server. Select the Config tab. In the left navigation menu, select SYSLOG to view the log file.

## Slide 23: Configure IOS Intrusion Prevention System

## Slide 24: Configure IOS Intrusion Prevention System
Step 5. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End