## Slide 1: Configuring Layer 2 Security
Network Security

## Slide 2: Configuring Layer 2 Security
Objectives of the Topic
After completing this topic, a student will be able to
  Configure Layer 2 security in Packet tracer.

## Slide 3: Configuring Layer 2 Security
Figures and material in this topic have been adapted from
Chapter 6: PT Activity: Layer 2 Security – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configuring Layer 2 Security
Experimental Setup:
Assume that your company’s network administrator has assigned you the task of configuring Layer 2 security.
For optimum performance and security, he has recommended that the root bridge is the 3560 Central switch and wants that the spanning tree protocol (STP- a Layer 2 link management protocol) parameters are secure against spanning-tree manipulation attacks.

## Slide 5: Configuring Layer 2 Security

## Slide 6: Configuring Layer 2 Security
To prevent broadcast storms, the network administrator wants you to enable storm control.
Finally, he has decided to configure port security to limit the number of MAC addresses that can be learned per switch port to prevent against MAC address table overflow attacks,.
In case, the number of MAC addresses exceeds the set limit, the administrator wants the port to be shutdown.

## Slide 7: Configuring Layer 2 Security
All switch devices have been preconfigured with the following:
Enable password: ciscoenpa55
Console password: ciscoconpa55
VTY line password: ciscovtypa55

## Slide 8: Configuring Layer 2 Security
Task 1: Configure Root Bridge
Step 1. Determine the current root bridge.
From Central, issue the show spanning-tree command to determine the current root bridge and to see the ports in use and their status.
Which switch is the current root-bridge?

## Slide 9: Configuring Layer 2 Security
Current root is SW-1

## Slide 10: Configuring Layer 2 Security
Step 2. Assign Central as the primary root bridge.
Use the spanning-tree vlan 1 root primary command to make the 3560 Central switch as the root bridge.
Central(config)# spanning-tree vlan 1 root primary
Step 3. Assign SW-1 as a secondary root bridge.
Use the spanning-tree vlan 1 root secondary command.

## Slide 11: Configuring Layer 2 Security
SW-1(config)# spanning-tree vlan 1 root secondary
Step 4. Verify the spanning-tree configuration.
Issue the show spanning-tree command to verify that 3560 Central switch is the root bridge.
Which switch is the current root-bridge? Current root is Central

## Slide 12: Configuring Layer 2 Security
Task 2: Protect Against STP Attacks
Secure the STP parameters to prevent STP manipulation attacks.
Step 1. Enable PortFast on all access ports.
PortFast is configured on access ports that connect to a single workstation or server to enable them to become active more quickly.
On the connected access ports of the SW-A and SW-B switches, use the spanning-tree portfast command.

## Slide 13: Configuring Layer 2 Security
SW-A(config)# interface range fastethernet 0/1 - 4
SW-A(config-if-range)# spanning-tree portfast
SW-B(config)# interface range fastethernet 0/1 - 4
SW-B(config-if-range)# spanning-tree portfast
Step 2. Enable BPDU guard on all access ports.
Bridge Protocol Data Unit (BPDU) guard is a feature that can help prevent rogue switches and spoofing on access ports.

## Slide 14: Configuring Layer 2 Security
Enable BPDU guard on SW-A and SW-B.
SW-A(config)# interface range fastethernet 0/1 - 4
SW-A(config-if-range)# spanning-tree bpduguard enable
SW-B(config)# interface range fastethernet 0/1 - 4
SW-B(config-if-range)# spanning-tree bpduguard enable

## Slide 15: Configuring Layer 2 Security
Step 3. Enable root guard.
Root guard can be enabled on all ports on a switch that are not root ports.
It is best deployed on ports that connect to other non-root switches.
Use the show spanning-tree command to determine the location of the root port on each switch.
On switch SW-1, enable root guard on ports Fa0/23 and Fa0/24. On switch SW-2, enable root guard on ports Fa0/23 and Fa0/24.

## Slide 16: Configuring Layer 2 Security
SW-1(config)# interface fa0/23
SW-1(config-if)# spanning-tree guard root
SW-1(config-if)# interface fa0/24
SW-1(config-if)# spanning-tree guard root
SW-2(config)# interface fa0/23
SW-2(config-if)# spanning-tree guard root
SW-2(config-if)# interface fa0/24
SW-2(config-if)# spanning-tree guard root

## Slide 17: Configuring Layer 2 Security
Task 3: Enable Storm Control
Step 1. Enable storm control for broadcasts.
Enable storm control for broadcasts on all ports connecting switches (trunk ports).
Set a 50 percent rising suppression level using the storm-control broadcast command.
Enable storm-control on interfaces connecting Central, SW-1, and SW-2.

## Slide 18: Configuring Layer 2 Security
SW-1(config)# interface gi1/1
SW-1(config-if)# storm-control broadcast level 50
SW-1(config-if)# interface fa0/1
SW-1(config-if)# storm-control broadcast level 50
SW-1(config-if)# interface fa0/23
SW-1(config-if)# storm-control broadcast level 50

## Slide 19: Configuring Layer 2 Security
SW-1(config-if)# interface fa0/24
SW-1(config-if)# storm-control broadcast level 50
Repeat on SW-2 (gig1/1, fa0/1, fa0/23, and fa0/24) and Central (gig0/1, gig0/2, fa0/1) connection to other switches

## Slide 20: Configuring Layer 2 Security
Step 2. Verify storm control configuration.
Verify your configuration with the show storm-control broadcast command and the show run command.
Task 4: Configure Port Security and Disable Unused Ports
Step 1. Configure basic port security on all ports connected to host devices.
This procedure should be performed on all access ports on SW-A and SW-B.

## Slide 21: Configuring Layer 2 Security
Set the maximum number of learned MAC address to 2, allow the MAC address to be learned dynamically, and set the violation to shutdown.
A switch port must be configured as an access port to enable port security.

## Slide 22: Configuring Layer 2 Security
SW-A(config)# interface FastEthernet 0/1
SW-A(config-if)# switchport mode access
SW-A(config-if)# switchport port-security
SW-A(config-if)# switchport port-security maximum 2
SW-A(config-if)# switchport port-security violation shutdown
SW-A(config-if)# switchport port-security mac-address sticky
Repeat on other ports in SW-A and SW-B

## Slide 23: Configuring Layer 2 Security
Why would you not want to enable port-security on ports connected to other switches or routers?
Ports connected to other switch devices and routers can, and should, have a multitude of MAC addresses learned for that single port.
Limiting the number of MAC addresses that can be learned on these ports can significantly impact network functionality.

## Slide 24: Configuring Layer 2 Security
Step 2. Verify port security.
On SW-A, issue the show port-security interface fa0/1 command to verify that port security has been configured.
Step 3. Disable unused ports.
Disable all ports that are currently unused.
SW-A(config)# interface FastEthernet 0/5
SW-A(config-if)# shutdown
Repeat on other ports on SW-A and SW-B

## Slide 25: Configuring Layer 2 Security
Step 4. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed.
End