## Slide 1: Configuring Layer 2 VLAN Security
Network Security

## Slide 2: Configuring Layer 2 VLAN Security
Objectives of the Topic
After completing this topic, a student will be able to
  Configure Layer 2 VLAN security in Packet tracer.

## Slide 3: Configuring Layer 2 VLAN Security
Figures and material in this topic have been adapted from
Chapter 6: PT Activity: Layer 2 VLAN Security – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configuring Layer 2 VLAN Security
Experimental Setup:
Lets assume that the network of a company is set up using two separate VLANs: VLAN 5 and VLAN 10.
All trunk ports are configured with VLAN 15.
The network administrator wants to add a redundant link between switch SW-1 and SW-2.
The link must have trunking enabled and all security requirements should be in place.

## Slide 5: Configuring Layer 2 VLAN Security

## Slide 6: Configuring Layer 2 VLAN Security
Also, the network administrator wants to connect a management PC to switch SW-A.
The administrator would like to allow the management PC to be able to connect to all switches and the router, but does not want any other devices to be able to connect to the management PC or the switches.
For management purposes, the administrator would like to create a new VLAN 20.

## Slide 7: Configuring Layer 2 VLAN Security
All devices have been preconfigured with:
Enable secret password: ciscoenpa55
Console password: ciscoconpa55
VTY line password: ciscovtypa55

## Slide 8: Configuring Layer 2 VLAN Security
Task 1: Verify Connectivity
Step 1. Verify connectivity between C2 (VLAN 10) and C3 (VLAN 10).
Step 2. Verify connectivity between C2 (VLAN 10) and D1 (VLAN 5).
If you are using the simple PDU GUI packet, ping twice to allow for ARP.

## Slide 9: Configuring Layer 2 VLAN Security
Task 2: Create a Redundant Link Between SW-1 and SW-2
Step 1. Connect SW-1 and SW-2.
Use a crossover cable to connect port Fa0/23 on SW-1 to port Fa0/23 on SW-2.
Step 2. Enable trunking, including all trunk security mechanisms on the link between SW-1 and SW-2.
Trunking has already been configured on all pre-existing trunk interfaces.

## Slide 10: Configuring Layer 2 VLAN Security
The new link must be configured for trunking, including all trunk security mechanisms. On both SW-1 and SW-2, set the port to trunk, assign native VLAN 15 to the trunk port, and disable auto-negotiation.
SW-1(config)# interface fa0/23
SW-1(config-if)# no shutdown
SW-1(config-if)# switchport mode trunk
SW-1(config-if)# switchport trunk native vlan 15
SW-1(config-if)# switchport nonegotiate

## Slide 11: Configuring Layer 2 VLAN Security
SW-1(config-if)# switchport nonegotiate
SW-2(config)# interface fa0/23
SW-2(config-if)# no shutdown
SW-2(config-if)# switchport mode trunk
SW-2(config-if)# switchport trunk native vlan 15
SW-2(config-if)# switchport nonegotiate

## Slide 12: Configuring Layer 2 VLAN Security
Task 3: Enable VLAN 20 as a Management VLAN
The network administrator would like to access all switch and routing devices using a management PC.
For security, the administrator wants to ensure that all managed devices are on a separate VLAN.

## Slide 13: Configuring Layer 2 VLAN Security
Step 1. Enable a management VLAN (VLAN 20) on SW-A.
Let’s use the default name of VLAN0020.
SW-A(config)# vlan 20
SW-A(config-vlan)# exit
Create an interface VLAN 20 and assign an IP address within the 192.168.20.0/24 network
SW-A(config)# interface vlan 20
SW-A(config-if)# ip address 192.168.20.1 255.255.255.0

## Slide 14: Configuring Layer 2 VLAN Security
Step 2. Enable the same management VLAN on all other switches.
Create the VLAN on all switches: SW-B, SW-1, SW-2 and Central.
SW-B(config)# vlan 20
SW-B(config-vlan)# exit
SW-B(config)# interface vlan 20
SW-B(config-if)# ip address 192.168.20.2 255.255.255.0

## Slide 15: Configuring Layer 2 VLAN Security
SW-1(config)# vlan 20
SW-1(config-vlan)# exit
SW-1(config)# interface vlan 20
SW-1(config-if)# ip address 192.168.20.3 255.255.255.0
SW-2(config)# vlan 20
SW-2(config-vlan)# exit
SW-2(config)# interface vlan 20
SW-2(config-if)# ip address 192.168.20.4 255.255.255.0

## Slide 16: Configuring Layer 2 VLAN Security
Central(config)# vlan 20
Central(config-vlan)# exit
Central(config)# interface vlan 20
Central(config-if)# ip address 192.168.20.5 255.255.255.0
Step 3. Configure the management PC and connect it to SW-A port Fa0/1.
Assign management PC an IP address within the 192.168.20.0/24 network and connect it to SW-A port Fa0/1.

## Slide 17: Configuring Layer 2 VLAN Security

## Slide 18: Configuring Layer 2 VLAN Security
Step 4. On SW-A, ensure the management PC is part of VLAN 20
Interface Fa0/1 must be part of VLAN 20.
SW-A(config)# interface fa0/1
SW-A(config-if)# switchport access vlan 20
SW-A(config-if)# no shutdown
Step 5. Verify connectivity of the management PC to all switches.
The management PC should be able to ping SW-A, SW-B, SW-1, SW-2 and Central.

## Slide 19: Configuring Layer 2 VLAN Security
Task 4: Enable the Management PC to Access Router R1
Step 1. Enable a new subinterface on router R1.
Create subinterface Fa0/0.3 and assign an IP address within the 192.168.20.0/24 network.
Set encapsulation to dot1q 20 to account for VLAN 20.

## Slide 20: Configuring Layer 2 VLAN Security
R1(config)# interface fa0/0.3
R1(config-subif)# encapsulation dot1q 20
R1(config-subif)# ip address 192.168.20.100 255.255.255.0
Step 2. Verify connectivity between the management PC and R1.
Configure the default gateway on the management PC to allow for connectivity.

## Slide 21: Configuring Layer 2 VLAN Security
Step 3. Enable security.
While the management PC must be able to access the router, no other PC should be able to access the management VLAN. Create an ACL(s) that denies any network from accessing the 192.168.20.0/24 network, but permits all other networks to access one another.
R1(config)# access-list 101 deny ip any 192.168.20.0 0.0.0.255
R1(config)# access-list 101 permit ip any any

## Slide 22: Configuring Layer 2 VLAN Security
Apply the ACL to the proper interface(s).
R1(config)# int fa0/0.1
R1(config-subif)# ip access-group 101 in
R1(config-subif)# int fa0/0.2
R1(config-subif)# ip access-group 101 in
The management PC must be able to connect to all switches and the router. All other PCs should not be able to connect to any devices within the management VLAN.

## Slide 23: Configuring Layer 2 VLAN Security
Step 4. Verify Security.
From the management PC, ping SW-A, SW-B, and R1. Was the ping successful?
The ping should have been successful because all devices within the 192.168.20.0 network should be able to ping one another.
Devices within VLAN20 are not required to route through the router.

## Slide 24: Configuring Layer 2 VLAN Security
From D1, ping the management PC. Was the ping successful?
The ping should have failed. This is because in order for a device within a different VLAN to successfully ping a device within VLAN20, it must be routed.
The router has an ACL that prevents all packets from accessing the 192.168.20.0 network.

## Slide 25: Configuring Layer 2 VLAN Security
Step 5. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and verification of which required components have been completed
End