## Slide 1: Configure & Verify a Site-to-Site IPsec VPN
Network Security

## Slide 2: Configure & Verify a Site-to-Site IPsec VPN
Objectives of the Topic
After completing this topic, a student will be able to
  Configure and Verify a Site-to-Site IPsec VPN in Packet tracer.

## Slide 3: Configure & Verify a Site-to-Site IPsec VPN
Figures and material in this topic have been adapted from
Chapter 8: PT Activity: Configure and Verify a Site-to-Site IPsec VPN using CLI – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure & Verify a Site-to-Site IPsec VPN
IPsec provides secure transmission of sensitive information over unprotected networks such as the Internet.
IPsec acts at the network layer, protecting and authenticating IP packets between participating IPsec devices (peers), such as Cisco routers.

## Slide 5: Configure & Verify a Site-to-Site IPsec VPN
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 6: Configure & Verify a Site-to-Site IPsec VPN

## Slide 7: Configure & Verify a Site-to-Site IPsec VPN
We want to configure routers R1 and R3 to support a site-to-site IPsec VPN when traffic flows from their respective LANs.
The IPsec VPN tunnel is from router R1 to router R3 via R2.
R2 acts as a pass-through and has no knowledge of the VPN.

## Slide 8: Configure & Verify a Site-to-Site IPsec VPN
The routers are already configured with the following settings:
Password for console line: ciscoconpa55
Password for vty lines: ciscovtypa55
Enable password: ciscoenpa55
RIP version 2

## Slide 9: Configure & Verify a Site-to-Site IPsec VPN
Task 1: Configure IPsec parameters on R1
Step 1. Test connectivity.
Ping from PC-A to PC-C.
Step 2. Identify interesting traffic on R1.
Configure ACL 110 to identify the traffic from the LAN on R1 to the LAN on R3 as interesting.
This interesting traffic will trigger the IPsec VPN to be implemented whenever there is traffic between R1 to R3 LANs.

## Slide 10: Configure & Verify a Site-to-Site IPsec VPN
All other traffic sourced from the LANs will not be encrypted.
R1(config)# access-list 110 permit ip 192.168.1.0 0.0.0.255 192.168.3.0 0.0.0.255
Step 3. Configure the ISAKMP Phase1 properties on R1.
Configure the crypto ISAKMP policy 10 properties on R1 along with the shared crypto key vpnpa55.
Refer to the ISAKMP Phase 1 table for the specific parameters to configure.

## Slide 11: Configure & Verify a Site-to-Site IPsec VPN

## Slide 12: Configure & Verify a Site-to-Site IPsec VPN
We do not have to configure the default values.
The encryption, key exchange method, and DH method must be configured.
R1(config)# crypto isakmp policy 10
R1(config-isakmp)# encryption aes
R1(config-isakmp)# authentication pre-share
R1(config-isakmp)# group 2
R1(config-isakmp)# exit
R1(config)# crypto isakmp key vpnpa55 address 10.2.2.2

## Slide 13: Configure & Verify a Site-to-Site IPsec VPN
Step 4. Configure the ISAKMP Phase 2 properties on R1.
Create the transform-set VPN-SET to use esp-3des and esp-sha-hmac.
Then create the crypto map VPN-MAP that binds all of the Phase 2 parameters together.
Use sequence number 10 and identify it as an ipsec-isakmp map.
R1(config)# crypto ipsec transform-set VPN-SET esp-3des esp-sha-hmac

## Slide 14: Configure & Verify a Site-to-Site IPsec VPN

## Slide 15: Configure & Verify a Site-to-Site IPsec VPN
R1(config)# crypto map VPN-MAP 10 ipsec-isakmp
R1(config-crypto-map)# description VPN connection to R3
R1(config-crypto-map)# set peer 10.2.2.2
R1(config-crypto-map)# set transform-set VPN-SET
R1(config-crypto-map)# match address 110
R1(config-crypto-map)# exit

## Slide 16: Configure & Verify a Site-to-Site IPsec VPN
Step 5. Configure the crypto map on the outgoing interface.
Finally, bind the VPN-MAP crypto map to the outgoing Serial 0/0/0 interface.
R1(config)# interface S0/0/0
R1(config-if)# crypto map VPN-MAP

## Slide 17: Configure & Verify a Site-to-Site IPsec VPN
Task 2: Configure IPsec Parameters on R3
Step 1. Configure router R3 to support a site-to-site VPN with R1.
Now configure reciprocating parameters on R3. Configure ACL 110 identifying the traffic from the LAN on R3 to the LAN on R1 as interesting.
R3(config)# access-list 110 permit ip 192.168.3.0 0.0.0.255 192.168.1.0 0.0.0.255
Step 2. Configure the ISAKMP Phase 1 properties on R3.

## Slide 18: Configure & Verify a Site-to-Site IPsec VPN
Configure the crypto ISAKMP policy 10 properties on R3 along with the shared crypto key vpnpa55.
R3(config)# crypto isakmp policy 10
R3(config-isakmp)# encryption aes
R3(config-isakmp)# authentication pre-share
R3(config-isakmp)# group 2
R3(config-isakmp)# exit
R3(config)# crypto isakmp key vpnpa55 address 10.1.1.2

## Slide 19: Configure & Verify a Site-to-Site IPsec VPN
Step 3. Configure the ISAKMP Phase 2 properties on R1.
Like we did on R1, create the transform-set VPN-SET to use esp-3des and esp-sha-hmac.
Then create the crypto map VPN-MAP that binds all of the Phase 2 parameters together.
Use sequence number 10 and identify it as an ipsec-isakmp map.
R3(config)# crypto ipsec transform-set VPN-SET esp-3des esp-sha-hmac

## Slide 20: Configure & Verify a Site-to-Site IPsec VPN
R3(config)# crypto map VPN-MAP 10 ipsec-isakmp
R3(config-crypto-map)# description VPN connection to R1
R3(config-crypto-map)# set peer 10.1.1.2
R3(config-crypto-map)# set transform-set VPN-SET
R3(config-crypto-map)# match address 110
R3(config-crypto-map)# exit

## Slide 21: Configure & Verify a Site-to-Site IPsec VPN
Step 4. Configure the crypto map on the outgoing interface.
Finally, bind the VPN-MAP crypto map to the outgoing Serial 0/0/1 interface.
R3(config)# interface S0/0/1
R3(config-if)# crypto map VPN-MAP

## Slide 22: Configure & Verify a Site-to-Site IPsec VPN
Task 3: Verify the IPsec VPN
Step 1. Verify the tunnel prior to interesting traffic.
Issue the show crypto ipsec sa command on R1.
Notice that the number of packets encapsulated, encrypted, decapsulated and decrypted are all set to 0.

## Slide 23: Configure & Verify a Site-to-Site IPsec VPN

## Slide 24: Configure & Verify a Site-to-Site IPsec VPN
Step 2. Create interesting traffic.
From PC-A, ping PC-C.
Step 3. Verify the tunnel after interesting traffic.
On R1, re-issue the show crypto ipsec sa command. Now notice that the number of packets is more than 0 indicating that the IPsec VPN tunnel is working.

## Slide 25: Configure & Verify a Site-to-Site IPsec VPN

## Slide 26: Configure & Verify a Site-to-Site IPsec VPN
Step 4. Create uninteresting traffic .
From PC-A, ping PC-B.
Step 5. Verify the tunnel.
On R1, re-issue the show crypto ipsec sa. We can find that number of packets has not changed.
Step 6. Check results.
Your completion percentage should be 100%.
Click Check Results to see feedback and to see which components have been completed.