## Slide 1: Configure a Network for Secure Operation-1
Network Security

## Slide 2: Configure a Network for Secure Operation-1
Objectives of the Topic
After completing this topic, a student will be able to
  Configure a Network for Secure Operation in Packet tracer.

## Slide 3: Configure a Network for Secure Operation-1
Figures and material in this topic have been adapted from
Chapter 9: PT Activity: Configure a Network for Secure Operation – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure a Network for Secure Operation-1
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 5: Configure a Network for Secure Operation-1

## Slide 6: Configure a Network for Secure Operation-1
In the topology, R1 is the edge router for the Company A while R3 is the edge router for Company B.
These networks are interconnected via the R2 router which represents the ISP.
The following preconfigurations have been made:
Hostnames on all devices
IP addresses on all devices
R2 console password: ciscoconpa55

## Slide 7: Configure a Network for Secure Operation-1
R2 password on VTY lines: ciscovtypa55
R2 enable password: ciscoenpa55
Static routing
Syslog services on PC-B
DNS lookup has been disabled
IP default gateways for all switches

## Slide 8: Configure a Network for Secure Operation-1
Task 1: Test Connectivity and Verify Configurations
Step 1. Verify IP addresses.
R1# show ip interface brief
R1# show run
Step 2. Verify routing tables.
R1# show ip route
Step 3. Test connectivity.
From PC-A, ping PC-C at IP address 192.168.3.5.

## Slide 9: Configure a Network for Secure Operation-1
Task 2: Secure the Routers
Step 1. Set minimum a password length of 10 characters on router R1 and R3.
R1(config)# security passwords min-length 10
R3(config)# security passwords min-length 10
Step 2. Configure an enable secret password on router R1 and R3.
Use an enable secret password of ciscoenpa55.
R1(config)# enable secret ciscoenpa55
R3(config)# enable secret ciscoenpa55

## Slide 10: Configure a Network for Secure Operation-1
Step 3. Encrypt plaintext passwords .
R1(config)# service password-encryption
R3(config)# service password-encryption
Step 4. Configure the console lines on R1 and R3.
Configure a console password of ciscoconpa55 and enable login. Set the exec-timeout to log out after 5 minutes of inactivity. Prevent console messages from interrupting command entry.

## Slide 11: Configure a Network for Secure Operation-1
R1(config)# line console 0
R1(config-line)# password ciscoconpa55
R1(config-line)# exec-timeout 5 0
R1(config-line)# login
R1(config-line)# logging synchronous
Repeat the above on R3.
Step 5. Configure vty lines on R1.
Configure a vty line password of ciscovtypa55 and enable login. Set the exec-timeout to log out after 5 minutes of inactivity.

## Slide 12: Configure a Network for Secure Operation-1
Set the login authentication to use the default AAA list to be defined later.
R1(config)# line vty 0 4
R1(config-line)# password ciscovtypa55
R1(config-line)# exec-timeout 5 0
R1(config-line)# login authentication default
Step 6. Configure login banner on R1 and R3.
Configure a warning to unauthorized users with a message-of-the-day (MOTD) banner that says: “No Unauthorized Access!”.

## Slide 13: Configure a Network for Secure Operation-1
R1(config)# banner motd $No Unauthorized Access!$
R3(config)# banner motd $No Unauthorized Access!$
Task 3: Configure Local Authentication on R1 and R3
Step 1. Configure the local user database.
Create a local user account of Admin01 with a secret password of Admin01pa55.

## Slide 14: Configure a Network for Secure Operation-1
R1(config)# username Admin01 privilege 15 secret Admin01pa55
R3(config)# username Admin01 privilege 15 secret Admin01pa55
Step 2. Enable AAA services.
R1(config)# aaa new-model
R3(config)# aaa new-model
Step 3. Implement AAA services using the local database.

## Slide 15: Configure a Network for Secure Operation-1
Create the default login authentication method list using local authentication with no backup method.
R1(config)# aaa authentication login default local none
R3(config)# aaa authentication login default local none
Task 4: Configure NTP
Step 1. Enable NTP authentication on PC-A.

## Slide 16: Configure a Network for Secure Operation-1
On PC-A, choose the Config tab, and then the NTP button. Select On for NTP service. Enable authentication and enter a Key of 1 and a password of ciscontppa55.
Step 2. Configure R1 as an NTP Client.
Configure NTP authentication Key 1 with a password of ciscontppa55. Configure R1 to synchronize with the NTP server and authenticate using Key 1.
R1(config)# ntp authenticate

## Slide 17: Configure a Network for Secure Operation-1
R1(config)# ntp authentication-key 1 md5 ciscontppa55
R1(config)# ntp trusted-key 1
R1(config)# ntp server 192.168.1.5 key 1
Step 3. Configure routers to update hardware clock.
R1(config)# ntp update-calendar
Task 5: Configure R1 as Syslog Client
Step 1. Configure R1 to timestamp log messages .

## Slide 18: Configure a Network for Secure Operation-1
R1(config)# service timestamps log datetime msec
Step 2. Configure R1 to log messages to the syslog server.
R1(config)# logging 192.168.1.6
Step 3. Check for syslog messages on PC-B.
On R1, exit config mode to generate a syslog message. Open the syslog server on PC-B to view the message sent from R1.

## Slide 19: Configure a Network for Secure Operation-1
Task 6: Secure Router Against Login Attacks
Step 1. Log unsuccessful login attempts to R1.
R1(config)# login on-failure log
Step 2. Telnet to R1 from PC-A.
Provide the username Admin01 and password Admin01pa55. The Telnet should be successful.
Step 3. Telnet to R1 from PC-A and check syslog messages on the syslog server.
Exit from the current Telnet session and Telnet again to R1.

## Slide 20: Configure a Network for Secure Operation-1
This time, use the username of baduser and any password. Check the syslog server on PC-B. You should see an error message.
Task 7: Configure SSH on R3
Step 1. Configure a domain name.
R3(config)# ip domain-name ccnasecurity.com
Step 2. Configure the incoming vty lines on R3.
Use the local user accounts for mandatory login and validation and accept only SSH connections.

## Slide 21: Configure a Network for Secure Operation-1
R3(config)# line vty 0 4
R3(config-line)# exec-timeout 5 0
R3(config-line)# login local
R3(config-line)# transport input ssh
Step 3. Configure RSA encryption key pair for R3.
R3(config)# crypto key zeroize rsa
% No Signature RSA Keys found in configuration.
R3(config)# crypto key generate rsa [Enter]

## Slide 22: Configure a Network for Secure Operation-1
The name for the keys will be: R3.ccnasecurity.com
Choose the size of the key modulus in the range of 360 to 2048 for your General Purpose Keys. Choosing a key modulus greater than 512 may take a few minutes.
How many bits in the modulus [512]:1024
% Generating 1024 bit RSA keys, keys will be non-exportable...[OK]
Step 4. Configure SSH timeouts and authentication parameters.

## Slide 23: Configure a Network for Secure Operation-1
Set SSH timeout to 90 seconds, the number of authentication retries to 2, and the version to 2.
R3(config)# ip ssh time-out 90
R3(config)# ip ssh authentication-retries 2
R3(config)# ip ssh version 2
Task 8: Configure CBAC on R1
Step 1. Configure a named IP ACL .
R1(config)# ip access-list extended OUT-IN
R1(config-ext-nacl)# deny ip any any
R1(config-ext-nacl)# exit

## Slide 24: Configure a Network for Secure Operation-1
R1(config)# interface s0/0/0
R1(config-if)# ip access-group OUT-IN in
Step 2. Confirm that traffic entering interface Serial 0/0/0 is dropped.
From the PC-A command prompt, ping PC-C. The ICMP echo replies are blocked by the ACL.
Step 3. Create an inspection rule to inspect ICMP, Telnet and HTTP traffic.

## Slide 25: Configure a Network for Secure Operation-1
R1(config)# ip inspect name IN-OUT-IN icmp
R1(config)# ip inspect name IN-OUT-IN telnet
R1(config)# ip inspect name IN-OUT-IN http
Step 4. Apply the inspect rule to the outside interface.
R1(config)# interface s0/0/0
R1(config-if)# ip inspect IN-OUT-IN out
Step 5. Test operation of the inspection rule.
From the PC-A command prompt, ping PC-C.

## Slide 26: Configure a Network for Secure Operation-1
The ICMP echo replies should be inspected and allowed through.
Task 9: Configure ZPF on R3
Step 1. Test connectivity.
Verify that the internal host can access external resources.
From PC-C, test connectivity with ping and Telnet to R2; all should be successful.
From R2 ping to PC-C. The pings should be allowed.

## Slide 27: Configure a Network for Secure Operation-1
Step 2. Create the firewall zones.
Create an internal zone named IN-ZONE.
R3(config)# zone security IN-ZONE
Create an external zone named OUT-ZONE.
R3(config)# zone security OUT-ZONE
Step 3. Create an ACL that defines internal traffic. Create an extended, numbered ACL that permits all IP protocols from 192.168.3.0/24 source network to any destination. Use 101 for the ACL number.

## Slide 28: Configure a Network for Secure Operation-1
R3(config)# access-list 101 permit ip 192.168.3.0 0.0.0.255 any
Step 4. Create a class map referencing the internal traffic ACL.
Create a class map named IN-NET-CLASS-MAP to match ACL 101.
R3(config)# class-map type inspect match-all IN-NET-CLASS-MAP
R3(config-cmap)# match access-group 101
R3(config-cmap)# exit

## Slide 29: Configure a Network for Secure Operation-1
Step 5. Specify firewall policies.
Create a policy map named IN-2-OUT-PMAP to determine what to do with matched traffic.
R3(config)# policy-map type inspect IN-2-OUT-PMAP
Specify a class type of inspect and reference class map IN-NET-CLASS-MAP.
R3(config-pmap)# class type inspect IN-NET-CLASS-MAP
Specify the action of inspect for this policy map

## Slide 30: Configure a Network for Secure Operation-1
R3(config-pmap-c)# inspect
You should see the following console message:
%No specific protocol configured in class IN-NET-CLASS-MAP for inspection. All protocols will be inspected.”
Exit to the global config prompt.
R3(config-pmap-c)# exit
R3(config-pmap)# exit
Step 6. Apply firewall policies.

## Slide 31: Configure a Network for Secure Operation-1
Create a zone pair named IN-2-OUT-ZPAIR. Specify the source and destination zones that were created earlier.
R3(config)# zone-pair security IN-2-OUT-ZPAIR source IN-ZONE destination OUT-ZONE
Attach a policy map and actions to the zone pair referencing the policy map previously created, IN-2-OUTPMAP.
R3(config-sec-zone-pair)# service-policy type inspect IN-2-OUT-PMAP

## Slide 32: Configure a Network for Secure Operation-1
Exit to the global config prompt and assign the internal and external interfaces to the security zones.
R3(config)# interface fa0/1
R3(config-if)# zone-member security IN-ZONE
R3(config-if)# interface s0/0/1
R3(config-if)# zone-member security OUT-ZONE
Step 7. Test firewall functionality.

## Slide 33: Configure a Network for Secure Operation-1
Verify that the internal host can still access external resources.
From PC-C, test connectivity with ping and Telnet to R2; all should be successful.
From R2 ping to PC-C. The pings should now be blocked.