## Slide 1: Configure a Network for Secure Operation-2
Network Security

## Slide 2: Configure a Network for Secure Operation-2
Objectives of the Topic
After completing this topic, a student will be able to
  Configure a Network for Secure Operation in Packet tracer.

## Slide 3: Configure a Network for Secure Operation-2
Figures and material in this topic have been adapted from
Chapter 9: PT Activity: Configure a Network for Secure Operation – “CCNA Security 1.1 Student Packet Tracer Manual”, Cisco 2012.

## Slide 4: Configure a Network for Secure Operation-2
Experimental Setup: Lets assume a network topology consists of three routers R1, R2 and R3.

## Slide 5: Configure a Network for Secure Operation-2
Task 10: Secure the Switches
Step 1. Configure an enable secret password on all switches.
Use an enable secret password of ciscoenpa55.
S1(config)# enable secret ciscoenpa55
Step 2. Encrypt plaintext passwords .
S1(config)# service password-encryption
Step 3. Configure the console lines on all switches.

## Slide 6: Configure a Network for Secure Operation-2
Configure a console password of ciscoconpa55 and enable login. Set the exec-timeout to log out after 5 minutes of inactivity. Prevent console messages from interrupting command entry.
S1(config)# line console 0
S1(config-line)# password ciscoconpa55
S1(config-line)# exec-timeout 5 0
S1(config-line)# login
S1(config-line)# logging synchronous

## Slide 7: Configure a Network for Secure Operation-2
Step 4. Configure vty lines on all switches .
Configure a vty line password of ciscovtypa55 and enable login. Set the exec-timeout to log out after 5 minutes of inactivity. Set the basic login parameter.
S1(config)# line vty 0 4
S1(config-line)# password ciscovtypa55
S1(config-line)# exec-timeout 5 0
S1(config-line)# login

## Slide 8: Configure a Network for Secure Operation-2
Step 5. Secure trunk ports on S1 and S2.
Configure port Fa0/1 on S1 as a trunk port.
S1(config)# interface FastEthernet 0/1
S1(config-if)# switchport mode trunk
Repeat for S2.
Verify that S1 port Fa0/1 is in trunking mode.
S1# show interfaces trunk
Set the native VLAN on S1 and S2 trunk ports to an unused VLAN 99.

## Slide 9: Configure a Network for Secure Operation-2
S1(config)# interface Fa0/1
S1(config-if)# switchport trunk native vlan 99
S1(config-if)# end
Repeat for S2.
Set the trunk ports on S1 and S2 so that they do not negotiate by turning off the generation of DTP frames.
S1(config)# interface Fa0/1
S1(config-if)# switchport nonegotiate
Repeat for S2.

## Slide 10: Configure a Network for Secure Operation-2
Enable storm control for broadcasts on the S1 and S2 trunk ports with a 50 percent rising suppression level.
S1(config)# interface FastEthernet 0/1
S1(config-if)# storm-control broadcast level 50
Repeat for S2.
Step 6. Secure access ports.
S1(config)# interface FastEthernet 0/5
S1(config-if)# switchport mode access

## Slide 11: Configure a Network for Secure Operation-2
Repeat for S1 FastEthernet 0/6, S2 FastEthernet 0/18, S3 FastEthernet 0/5, and S3 FastEthernet 0/6.
Enable PortFast on S1, S2, and S3 access ports.
S1(config)# interface FastEthernet 0/5
S1(config-if)# spanning-tree portfast
Repeat for S1 FastEthernet 0/6, S2 FastEthernet 0/18, S3 FastEthernet 0/5, and S3 FastEthernet 0/6.

## Slide 12: Configure a Network for Secure Operation-2
Enable BPDU guard on the switch ports previously configured as access only.
S1(config)# interface FastEthernet 0/5
S1(config-if)# spanning-tree bpduguard enable
Repeat for S1 FastEthernet 0/6, S2 FastEthernet 0/18, S3 FastEthernet 0/5, and S3 FastEthernet 0/6.
Enable basic default port security on all end-user access ports that are in use. Use the sticky option. Reenable each access port to which port security was applied.

## Slide 13: Configure a Network for Secure Operation-2
S1(config)# interface FastEthernet 0/5
S1(config-if)# shutdown
S1(config-if)# switchport port-security
S1(config-if)# switchport port-security mac-address sticky
S1(config-if)# no shutdown
Repeat for S1 FastEthernet 0/6, S2 FastEthernet 0/18, S3 FastEthernet 0/5, and S3 FastEthernet 0/6.

## Slide 14: Configure a Network for Secure Operation-2
Disable any ports not being used on each switch.

## Slide 15: Configure a Network for Secure Operation-2
Task 11: Verification
Step 1. Test SSH configuration.
Attempt to connect to R3 via Telnet from PC-C.
From PC-C, enter the command to connect to R3 via Telnet at IP address 192.168.3.1. This connection should fail, since R3 has been configured to accept only SSH connections on the virtual terminal lines.

## Slide 16: Configure a Network for Secure Operation-2
From PC-C, enter the ssh –l Admin01 192.168.3.1 command to connect to R3 via SSH.
When prompted for the password, enter the password Admin01pa55 configured for the local administrator.
Use the show ip ssh command to see the configured settings.
R3# show ip ssh
SSH Enabled - version 2.0, Authentication timeout: 90 secs; Authentication retries: 2

## Slide 17: Configure a Network for Secure Operation-2
Step 2. Verify timestamps , NTP status for R1 and PC-A.
R1# show clock
R1# show ntp status
Step 3. Test CBAC firewall on R1.
Ping from PC-A to R2 at 10.2.2.2 (should succeed). Telnet from PC-A to R2 10.2.2.2 (should succeed). Ping from R2 to PC-A at 192.168.1.3 (should fail)

## Slide 18: Configure a Network for Secure Operation-2
Step 4. Test ZPF firewall on R3.
Ping from PC-C to R2 at 10.2.2.2 (should succeed)
Telnet from PC-C to R2 at 10.2.2.2 (should succeed)
Ping from R2 to PC-C at 192.168.3.5 (should fail)
Telnet from R2 to R3 at 10.2.2.1 (should fail – only SSH is allowed)

## Slide 19: Configure a Network for Secure Operation-2
Step 5. Verify port security.
On S2, use the show run command to confirm that S2 has added a sticky MAC address for Fa0/18. This should be the MAC address of PC-B. Record the MAC address for later use.
S2#show run
Select PC-B. Go to the Config tab. Select FastEthernet under the Interface section. Edit the MAC address field. For example, change it from 0001.435D.3057 to 0001.435D.AAAA.

## Slide 20: Configure a Network for Secure Operation-2
This should cause a port security violation and S2 should shut down port Fa0/18.
Use the show interface Fa0/18 command to view the status of the port. The port should be in the err-disabled state.
S2#show int fa0/18
S2#show port-security
On PC-B, go to the Config tab. Select FastEthernet under the Interface section. Change the MAC address to another address.

## Slide 21: Configure a Network for Secure Operation-2
For example, change it from 0001.435D.AAAA to 0001.435D.BBBB.
From interface configuration mode on switch S2 for Fa0/18, use the no switchport port-security macaddress sticky address command to remove the original PC-B learned address.
S2(config)# int fa0/18
S2(config-if)# no switchport port-security mac-address sticky 0001.435D.3057

## Slide 22: Configure a Network for Secure Operation-2
Shutdown and then re-enable the Fa0/18 interface.
S2(config)# int fa0/18
S2(config-if)# shutdown
S2(config-if)# no shutdown
On S2, use the show run command to confirm that the port comes up and that the new MAC address has been learned.
S2#show run

## Slide 23: Configure a Network for Secure Operation-2
Step 6. Check results.
Your completion percentage should be 100%. Click Check Results to see feedback and verification of which required components have been completed.