## Slide 1: SSH Connection Protocol
Network Security

## Slide 2: SSH Connection Protocol
Objectives of the Topic
After completing this topic, a student will be able to
  describe working of the SSH Connection Protocol.

## Slide 3: SSH Connection Protocol
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: SSH Connection Protocol
The SSH Connection Protocol runs on top of the SSH Transport Layer Protocol and assumes that a secure authentication connection is in use.
Connection, referred to as a tunnel, is used to multiplex a number of logical channels.

## Slide 5: SSH Connection Protocol
Channel Mechanism:
All types of communication using SSH, such as a terminal session, are supported using separate channels.
Either side may open a channel.

## Slide 6: SSH Connection Protocol
For each channel, each side associates a unique channel number, which need not be the same on both ends.

## Slide 7: SSH Connection Protocol
Channels are flow controlled using a window mechanism.
No data may be sent to a channel until a message is received to indicate that window space is available.

## Slide 8: SSH Connection Protocol
The life of a channel progresses through three stages:
opening a channel,
data transfer, and
closing a channel.

## Slide 9: SSH Connection Protocol
When either side wishes to open a new channel, it allocates a local number for the channel and then sends a message of the form:

## Slide 10: SSH Connection Protocol
where uint32 means unsigned 32-bit integer.
The channel type identifies the application for this channel.
The sender channel is the local channel number.

## Slide 11: SSH Connection Protocol
The initial window size specifies how many bytes of channel data can be sent to the sender of this message without adjusting the window.
The maximum packet size specifies the maximum size of an individual data packet that can be sent to the sender.

## Slide 12: SSH Connection Protocol
If the remote side is able to open the channel, it returns a SSH_MSG_CHANNEL_OPEN_CONFIRMATION, which includes the sender channel number, the recipient channel number, and window and packet size values for incoming traffic.

## Slide 13: SSH Connection Protocol
Otherwise, the remote side returns a SSH_MSG_CHANNEL_OPEN_FAILURE message with a reason code indicating the reason for failure.

## Slide 14: SSH Connection Protocol
Once a channel is open, data transfer is performed using a SSH_MSG_CHANNEL_DATA message, which includes the recipient channel number and a block of data.

## Slide 15: SSH Connection Protocol
These messages, in both directions, may continue as long as the channel is open.
When either side wishes to close a channel, it sends a SSH_MSG_CHANNEL_CLOSE message (includes recipient channel number).

## Slide 16: SSH Connection Protocol
An Example

## Slide 17: SSH Connection Protocol
Channel Types:
Four channel types are recognized in the SSH Connection Protocol specification.
session: The remote execution of a program.

## Slide 18: SSH Connection Protocol
The program may be a shell, an application such as file transfer or e-mail, a system command, or some built-in subsystem.
Once a session channel is opened, subsequent requests are used to start the remote program.

## Slide 19: SSH Connection Protocol
x11: refers to the X Window System, a computer software system and network protocol that provides a graphical user interface (GUI) for networked computers.

## Slide 20: SSH Connection Protocol
X allows applications to run on a network server but to be displayed on a desktop machine.
forwarded-tcpip: This is remote port forwarding.
direct-tcpip: This is local port forwarding.
End