## Slide 1: Wireless Network Security Measures
Network Security

## Slide 2: Wireless Network Security Measures
Objectives of the Topic
After completing this topic, a student will be able to
  describe security measures for a wireless network.

## Slide 3: Wireless Network Security Measures
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: Wireless Network Security Measures
We can group wireless security measures along three dimensions.

## Slide 5: Wireless Network Security Measures
1.Securing Wireless Transmissions:
The principal threats to wireless transmission are eavesdropping, altering or inserting messages, and disruption.

## Slide 6: Wireless Network Security Measures
To deal with eavesdropping, two types of countermeasures are appropriate:
A. Signal-hiding technique:
turn off service set identifier (SSID) broadcasting by wireless access points

## Slide 7: Wireless Network Security Measures
Assign cryptic names to SSIDs.
Reduce signal strength to the lowest level that still provides requisite coverage.
Locate wireless access points in the interior of the building, away from windows and exterior walls.

## Slide 8: Wireless Network Security Measures
B. Encryption
is effective against eavesdropping to the extent that the encryption keys are secured.

## Slide 9: Wireless Network Security Measures
The use of encryption and authentication protocols is the standard method of countering attempts to alter or insert transmissions.

## Slide 10: Wireless Network Security Measures
2. Securing Wireless Access Points
The main threat involving wireless access points is unauthorized access to the network.

## Slide 11: Wireless Network Security Measures
The principal approach for preventing such access is the IEEE 802.1X standard for port-based network access control.

## Slide 12: Wireless Network Security Measures
IEEE 802.1X standard provides an authentication mechanism for devices wishing to attach to a LAN or a wireless network.

## Slide 13: Wireless Network Security Measures
The use of IEEE 802.1X can prevent rogue access points and other unauthorized devices from becoming insecure backdoors.

## Slide 14: Wireless Network Security Measures
Securing Wireless Networks:
Following techniques are recommended for wireless network security:

## Slide 15: Wireless Network Security Measures
1. Use encryption:
Wireless routers are typically equipped with built-in encryption mechanisms for router-to-router traffic.

## Slide 16: Wireless Network Security Measures
2. Use antivirus and antispyware software, and a firewall:
These facilities should be enabled on all wireless network endpoints.

## Slide 17: Wireless Network Security Measures
3. Turn off identifier broadcasting:
Wireless routers are typically configured to broadcast an identifying signal so that any device within range can learn of the router’s existence.

## Slide 18: Wireless Network Security Measures
If a network is configured so that authorized devices know the identity of routers, this capability can be disabled, so as to thwart attackers.

## Slide 19: Wireless Network Security Measures
4. Change the identifier on your router from the default:
This measure thwarts attackers who will attempt to gain access to a wireless network using default router identifiers.

## Slide 20: Wireless Network Security Measures
5. Change your router’s pre-set password for administration:
This is another prudent step.

## Slide 21: Wireless Network Security Measures
6. Allow only specific computers to access your wireless network: A router can be configured to only communicate with approved MAC addresses, which can be spoofed, so this is just one element of a security strategy.
End