## Slide 1: IEEE 802 Protocol Architecture
Network Security

## Slide 2: IEEE 802 Protocol Architecture
Objectives of the Topic
After completing this topic, a student will be able to
  Describe Architecture of IEEE 802 Protocol.

## Slide 3: IEEE 802 Protocol Architecture
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: IEEE 802 Protocol Architecture
IEEE 802.11 standards are defined within the structure of a layered set of protocols.
This structure, used for all IEEE 802 standards, is illustrated next.

## Slide 5: IEEE 802 Protocol Architecture
IEEE 802.11 Protocol Stack

## Slide 6: IEEE 802 Protocol Architecture
Physical Layer
The lowest layer of the IEEE 802 reference model is the physical layer, which includes such functions as encoding/decoding of signals and bit transmission/ reception.

## Slide 7: IEEE 802 Protocol Architecture
In addition, the physical layer includes a specification of the transmission medium.
In the case of IEEE 802.11, the physical layer also defines frequency bands and antenna characteristics.

## Slide 8: IEEE 802 Protocol Architecture
Media Access Control:
All LANs consist of collections of devices that share the network’s transmission capacity.

## Slide 9: IEEE 802 Protocol Architecture
Some means of controlling access to the transmission medium is needed to provide an orderly and efficient use of that capacity.
This is the function of a media access control (MAC) layer.

## Slide 10: IEEE 802 Protocol Architecture
The MAC layer receives data from a higher-layer protocol, typically the Logical Link Control (LLC) layer, in the form of a block of data known as the MAC service data unit (MSDU).

## Slide 11: IEEE 802 Protocol Architecture
In general, the MAC layer performs the following functions:
1. On transmission, assemble data into a frame, known as a MAC protocol data unit (MPDU) with address and error-detection fields.

## Slide 12: IEEE 802 Protocol Architecture
2. On reception, disassemble frame, and perform address recognition and error detection.
3. Govern access to the LAN transmission medium.

## Slide 13: IEEE 802 Protocol Architecture
The exact format of the MPDU differs somewhat for the various MAC protocols in use.
All of the MPDUs have a similar format in general.
The fields of this frame are as follows.

## Slide 14: IEEE 802 Protocol Architecture
General IEEE 802 MPDU Format

## Slide 15: IEEE 802 Protocol Architecture
MAC Control: This field contains any protocol control information needed for the functioning of the MAC protocol.
For example, a priority level could be indicated here.

## Slide 16: IEEE 802 Protocol Architecture
Destination MAC Address: The destination physical address on the LAN for this MPDU.
Source MAC Address: The source physical address on the LAN for this MPDU.

## Slide 17: IEEE 802 Protocol Architecture
MAC Service Data Unit: The data from the next higher layer.
CRC: The cyclic redundancy check field; also known as the Frame Check Sequence (FCS) field.
This is an error-detecting code.

## Slide 18: IEEE 802 Protocol Architecture
The CRC is calculated based on the bits in the entire MPDU.
The sender calculates the CRC and adds it to the frame.

## Slide 19: IEEE 802 Protocol Architecture
The receiver performs the same calculation on the incoming MPDU and compares that calculation to the CRC field in that incoming MPDU.
If the two values don’t match, then one or more bits have been altered in transit.

## Slide 20: IEEE 802 Protocol Architecture
The MAC header and MAC trailer contain control information that accompany the data field and that are used by the MAC protocol.

## Slide 21: IEEE 802 Protocol Architecture
Logical Link Control In most data-link control protocols, the data-link protocol entity is responsible not only for detecting errors using the CRC, but for recovering from those errors by retransmitting damaged frames.

## Slide 22: IEEE 802 Protocol Architecture
In the LAN protocol architecture, these two functions are split between the MAC and LLC layers.
The MAC layer is responsible for detecting errors and discarding any frames that contain errors.

## Slide 23: IEEE 802 Protocol Architecture
The LLC layer optionally keeps track of which frames have been successfully received and retransmits unsuccessful frames.
End