## Slide 1: IEEE 802.11i Phases of Operation
Network Security

## Slide 2: IEEE 802.11i Phases of Operation
Objectives of the Topic
After completing this topic, a student will be able to
  explain IEEE 802.11i Phases of Operation.

## Slide 3: IEEE 802.11i Phases of Operation
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: IEEE 802.11i Phases of Operation
The operation of an IEEE 802.11i RSN can be broken down into five distinct phases of operation.
The exact nature of the phases will depend on the configuration and the end points of the communication.

## Slide 5: IEEE 802.11i Phases of Operation
Possibilities include:
1. Two wireless stations in the same BSS communicating via the access point (AP) for that BSS.

## Slide 6: IEEE 802.11i Phases of Operation
2. Two wireless stations (STAs) in the same ad hoc IBSS communicating directly with each other.

## Slide 7: IEEE 802.11i Phases of Operation
3. Two wireless stations in different BSSs communicating via their respective APs across a distribution system.

## Slide 8: IEEE 802.11i Phases of Operation
4. A wireless station communicating with an end station on a wired network via its AP and the distribution system.

## Slide 9: IEEE 802.11i Phases of Operation
IEEE 802.11i security is concerned only with secure communication between the STA and its AP.

## Slide 10: IEEE 802.11i Phases of Operation
In case 1 in the preceding list, secure communication is assured if each STA establishes secure communications with the AP.
Case 2 is similar, with the AP functionality residing in the STA.

## Slide 11: IEEE 802.11i Phases of Operation
For case 3, security is not provided across the distribution system at the level of IEEE 802.11, but only within each BSS.
End- to-end security (if required) must be provided at a higher layer.

## Slide 12: IEEE 802.11i Phases of Operation
Similarly, in case 4, security is only provided between the STA and its AP.
Next, we depict the five phases of operation for an RSN.

## Slide 13: IEEE 802.11i Phases of Operation
IEEE 802.11i Phases of Operation:

## Slide 14: IEEE 802.11i Phases of Operation
1. Discovery: An AP uses messages called Beacons and Probe Responses to advertise its IEEE 802.11i security policy.
STA uses these to identify an AP with which it wishes to communicate.

## Slide 15: IEEE 802.11i Phases of Operation
The STA associates with the AP, which it uses to select the cipher suite and authentication mechanism when the Beacons and Probe Responses present a choice.

## Slide 16: IEEE 802.11i Phases of Operation
2. Authentication: The STA and AS prove their identities to each other. The AP blocks non-authentication traffic between the STA and AS until the authentication transaction is successful.

## Slide 17: IEEE 802.11i Phases of Operation
3. Key generation and distribution: The AP and the STA perform several operations that cause cryptographic keys to be generated and placed on the AP and the STA.
Frames are exchanged between AP and STA.

## Slide 18: IEEE 802.11i Phases of Operation
4. Protected data transfer: Frames are exchanged between the STA and the end station through the AP.
Secure data transfer occurs between the STA and the AP only; security is not provided end-to-end.

## Slide 19: IEEE 802.11i Phases of Operation
5. Connection termination: The AP and STA exchange frames.
The secure connection is torn down and the connection is restored to the original state.
End