## Slide 1: Discovery Phase of IEEE 802.11i
Network Security

## Slide 2: Discovery Phase of IEEE 802.11i
Objectives of the Topic
After completing this topic, a student will be able to
  describe discovery phase of IEEE 802.11i.

## Slide 3: Discovery Phase of IEEE 802.11i
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: Discovery Phase of IEEE 802.11i
The purpose of this phase is for an STA and an AP to recognize each other, agree on a set of security capabilities, and establish an association for future communication using those security capabilities.

## Slide 5: Discovery Phase of IEEE 802.11i
Security Capabilities The STA and AP decide on specific techniques:
1.Confidentiality and MPDU integrity protocols for protecting unicast traffic (traffic only between this STA and AP).

## Slide 6: Discovery Phase of IEEE 802.11i
2.Authentication method
3.Cryptography key management approach

## Slide 7: Discovery Phase of IEEE 802.11i
Confidentiality and integrity protocols for protecting multicast/broadcast traffic are dictated by the AP, since all STAs in a multicast group must use the same protocols and ciphers.

## Slide 8: Discovery Phase of IEEE 802.11i
The specification of a protocol, along with the chosen key length (if variable) is known as a cipher suite.
The options for the confidentiality and integrity cipher suite are:

## Slide 9: Discovery Phase of IEEE 802.11i
WEP, with either a 40-bit or 104-bit key, which allows backward compatibility with older IEEE 802.11 implementations
TKIP
CCMP
Vendor-specific methods

## Slide 10: Discovery Phase of IEEE 802.11i
The other negotiable suite is authentication and key management suite, which defines (1) means by which AP and STA perform mutual authentication and (2) the means for deriving a root key from which other keys may be generated.

## Slide 11: Discovery Phase of IEEE 802.11i
The possible authentication and key management (AKM) suites are:

## Slide 12: Discovery Phase of IEEE 802.11i
IEEE 802.1X
Pre-shared key (no explicit authentication takes place and mutual authentication is implied if the STA and AP share a unique secret key)
Vendor-specific methods

## Slide 13: Discovery Phase of IEEE 802.11i
MPDU Exchange The discovery phase consists of three exchanges.
1.Network and security capability discovery: STAs discover the existence of a network with which to communicate.

## Slide 14: Discovery Phase of IEEE 802.11i
The AP either periodically broadcasts its security capabilities in a specific channel through the Beacon frame or responds to a station’s Probe Request through a Probe Response frame.

## Slide 15: Discovery Phase of IEEE 802.11i
A wireless station may discover available access points and corresponding security capabilities by either passively monitoring the Beacon frames or actively probing every channel.

## Slide 16: Discovery Phase of IEEE 802.11i
2.Open system authentication:
The two devices (STA and AP) simply exchange identifiers.
The purpose is simply to maintain backward compatibility with the IEEE 802.11.

## Slide 17: Discovery Phase of IEEE 802.11i
3.Association:
The purpose of this stage is to agree on a set of security capabilities to be used.
The STA then sends an Association Request frame to the AP.

## Slide 18: Discovery Phase of IEEE 802.11i
In this frame, the STA specifies one set of matching capabilities (one authentication and key management suite, one pairwise cipher suite, and one group-key cipher suite) from among those advertised by the AP.

## Slide 19: Discovery Phase of IEEE 802.11i
If there is no match in capabilities between the AP and the STA, the AP refuses the Association Request.
The STA blocks it too, in case it has associated with a rogue AP or someone is inserting frames illicitly on its channel.

## Slide 20: Discovery Phase of IEEE 802.11i