## Slide 1: Authentication Phase of IEEE 802.11i
Network Security

## Slide 2: Authentication Phase of IEEE 802.11i
Objectives of the Topic
After completing this topic, a student will be able to
  describe authentication phase of IEEE 802.11i.

## Slide 3: Authentication Phase of IEEE 802.11i
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: Authentication Phase of IEEE 802.11i
The authentication phase enables mutual authentication between an STA and an authentication server (AS) located in the DS.

## Slide 5: Authentication Phase of IEEE 802.11i
IEEE 802.1X Access Control Approach:
IEEE 802.11i makes use of IEEE 802.1X, Port-Based Network Access Control to provide access control functions for LANs.

## Slide 6: Authentication Phase of IEEE 802.11i
Extensible Authentication Protocol (EAP) is the authentication protocol that is used and is defined in the IEEE 802.1X standard.

## Slide 7: Authentication Phase of IEEE 802.11i
IEEE 802.1X uses the terms supplicant, authenticator, and authentication server (AS).
In the context of an 802.11 WLAN, the first two terms correspond to the wireless station and the AP.

## Slide 8: Authentication Phase of IEEE 802.11i
The AS is typically a separate device on the wired side of the network (i.e., accessible over the DS) but could also reside directly on the authenticator.

## Slide 9: Authentication Phase of IEEE 802.11i
For a WLAN, the authenticator (the AP) may have only two physical ports:
one connecting to the DS and one for wireless communication within its BSS.

## Slide 10: Authentication Phase of IEEE 802.11i
Each logical port (802.1X) is mapped to one of these two physical ports.
An uncontrolled port allows the exchange of PDUs between the supplicant and the other AS, regardless of authentication state of the supplicant.

## Slide 11: Authentication Phase of IEEE 802.11i
A controlled port allows the exchange of PDUs between a supplicant and other systems on the LAN only if the current state of the supplicant authorizes such an exchange.

## Slide 12: Authentication Phase of IEEE 802.11i
MPDU Exchange Following are the three phases:
1. Connect to AS: The STA sends a request to its AP for connection to the AS.
The AP acknowledges this request and sends an access request to the AS.

## Slide 13: Authentication Phase of IEEE 802.11i
2.EAP exchange: This exchange authenticates the STA and AS to each other.
3.Secure key delivery: AS generates a master session key (MSK) or the Authentication, Authorization, and Accounting (AAA) key and sends it to STA.

## Slide 14: Authentication Phase of IEEE 802.11i
All the cryptographic keys needed by STA for secure communication with its AP are generated from this MSK.
For secure delivery of MSK, an MPDU contains an encrypted MSK from the AS, via the AP, to the STA.

## Slide 15: Authentication Phase of IEEE 802.11i
EAP Exchange: Typically, message flow between STA and AP employs EAP over LAN (EAPOL), and the message flow between the AP and AS uses the Remote Authentication Dial In User Service (RADIUS) protocol.

## Slide 16: Authentication Phase of IEEE 802.11i
1. The AP issues an EAP-Request/Identity frame to the STA.
2. The STA replies with an EAP-Response/Identity frame, which the AP receives over the uncontrolled port.

## Slide 17: Authentication Phase of IEEE 802.11i
The packet is then encapsulated in RADIUS over EAP and passed on to the RADIUS server as a RADIUS-Access-Request packet.

## Slide 18: Authentication Phase of IEEE 802.11i
3. The AAA server replies with a RADIUS-Access-Challenge packet, which is passed on to the STA as an EAP-Request.
This request is of the appropriate authentication type.

## Slide 19: Authentication Phase of IEEE 802.11i
4. The STA formulates an EAP-Response message and sends it to the AS.
The response is translated by the AP into a Radius-Access-Request with the response to the challenge as a data field.

## Slide 20: Authentication Phase of IEEE 802.11i
Steps 3 and 4 may be repeated multiple times, depending on the EAP method in use.
5. The AAA server grants access with a Radius-Access-Accept packet.
The AP issues an EAP-Success frame.

## Slide 21: Authentication Phase of IEEE 802.11i
The controlled port is authorized, and the user may begin to access the network.

## Slide 22: Authentication Phase of IEEE 802.11i