## Slide 1: Protected Data Transfer of IEEE 802.11i
Network Security

## Slide 2: Protected Data Transfer of IEEE 802.11i
Objectives of the Topic
After completing this topic, a student will be able to
  describe Protected Data Transfer phase of IEEE 802.11i.

## Slide 3: Protected Data Transfer of IEEE 802.11i
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: Protected Data Transfer of IEEE 802.11i
IEEE 802.11i defines two schemes for protecting data transmitted in 802.11 MPDUs:
the Temporal Key Integrity Protocol (TKIP), and
the Counter Mode-CBC MAC Protocol (CCMP).

## Slide 5: Protected Data Transfer of IEEE 802.11i
TKIP:
TKIP is designed to require only software changes to devices that are implemented with the older wireless LAN security approach called Wired Equivalent Privacy (WEP).

## Slide 6: Protected Data Transfer of IEEE 802.11i
TKIP provides two services:
Message integrity: TKIP adds a message integrity code (MIC) to the 802.11 MAC frame after the data field.

## Slide 7: Protected Data Transfer of IEEE 802.11i
The MIC is generated by an algorithm, called Michael.
It computes a 64-bit value using as input the source and destination MAC address values and the Data field, plus key material.

## Slide 8: Protected Data Transfer of IEEE 802.11i
Data confidentiality:
is provided by encrypting the MPDU plus MIC value using RC4.
The 256-bit Temporal Key (TK) is employed as follows:

## Slide 9: Protected Data Transfer of IEEE 802.11i
Two 64-bit keys are used with the Michael message digest algorithm to produce a message integrity code.
One key is used to protect STA-to-AP messages, and the other key is used to protect AP-to-STA.

## Slide 10: Protected Data Transfer of IEEE 802.11i
The remaining 128 bits are truncated to generate the RC4 key used to encrypt the transmitted data.

## Slide 11: Protected Data Transfer of IEEE 802.11i
For additional protection, a monotonically increasing TKIP sequence counter (TSC) is assigned to each frame.
The TSC serves two purposes.

## Slide 12: Protected Data Transfer of IEEE 802.11i
First, the TSC is included with each MPDU and is protected by the MIC to protect against replay attacks.

## Slide 13: Protected Data Transfer of IEEE 802.11i
Second, the TSC is combined with the session TK to produce a dynamic encryption key that changes with each transmitted MPDU, thus making cryptanalysis more difficult.

## Slide 14: Protected Data Transfer of IEEE 802.11i
CCMP: CCMP is intended for newer IEEE 802.11 devices that are equipped with the hardware to support this scheme.
As with TKIP, CCMP provides two services:

## Slide 15: Protected Data Transfer of IEEE 802.11i
Message integrity:
CCMP uses the cipher block chaining message authentication code (CBC-MAC).

## Slide 16: Protected Data Transfer of IEEE 802.11i
Data confidentiality:
CCMP uses the CTR block cipher mode of operation with AES for encryption.

## Slide 17: Protected Data Transfer of IEEE 802.11i
The same 128-bit AES key is used for both integrity and confidentiality.
The scheme uses a 48-bit packet number to construct a nonce to prevent replay attacks.
End